## Slide 1: Adding artificial intelligence into process control systems – implementation and integration by open source tools
Tamás Ruppert1,2, Gyula Dörgő1,2, Dr. János Abonyi2
1 - Rabbit Miner Kft. 2 - Pannon Egyetem, MTA-PE Lendület Komplex Rendszerek Megfigyelő Kutató csoport
ruppert@rabbitminerlab.com
www.rabbitminerlab.com
www.abonyilab.com

## Slide 2
INFORMATION FLOW
MONEY FLOW
MATERIAL FLOW
Business management
Buying, selling, cash management, asset management, product management
Level 5
Business planning & logistics
planning & scheduling, production/logistic management
Level 4
Operations management
Detailed scheduling, reliability & availability assurance
Level 3
Procedure & Control execution
Automated Control / Monitoring
Level 2
Sensing & Manipulating
„Touch and feel of the process”
Level 1
Production execution
The actual production process
Level 0
Decision support system
KPIs - dynamical targeting
Smart monitoring (operator performances … business processes)
Improvement opportunities
Raw data
Machine learning
Performance model
Data-driven business development

## Slide 3
Hierarchy of the process
Deep learning
Sequence mining
Discrete events
State of the process
Frequent sequence mining for prediction
Alarm – operator interactions
Deep learning
Root cause analysis
Event prediction
Visualisation for interpretability
Hierarchy of the process
Structural process models
Helps the freq. seq. mining
Monitoring the spillover of malfunctions
Discrete events and states
Root cause analysis
Event (failure) prediction
Alarm suppression / automation
PAST
FUTURE
We have expertise in building data-driven models to:
detect the correlated alarm tags
develop predictive models to make an event prediction
make assumptions on the past and carry out a root cause analysis.
Alarm management

## Slide 4
ANSI/ISA – 18.2 Management of Alarm Systems for the Process Industries
Which alarms are necessary?
Measuring performance, KPIs
The alarm management lifecycle
Notes: The operator is in the focus ..
Provide exactly the right amount information
I recognised most people in this room know much more about …
For those who are less familiar with alarm management than me …
What is important on this slide is that … it shows our ambition that we want to develop tools …
To deterime the important, informative set of alarms
Reduce any redundancy .. Show the operators contectualised information
(so this means we would like to group … , supress ..

## Slide 5
Lane keeping
Cruise control
Smart routing
Computer vision
Predictive decision making
Predictive maintenance
Safety
Lane keeping – line keeping
Cruise control – Pressure control
Smart routing – Smart workinstruction
Computer vision
Predictive decision making
Predictive maintenance
Safety
Self-driving car/operator

## Slide 6
From | To | Production Unit | Unit | Tag | Event Type | Description
10/24/2018 16:02 | 10/24/2018 16:04 | Distillation | Main column | Head temp. | Alarm | High alarm
10/24/2018 16:02 | 10/24/2018 16:04 | Distillation | Main column | Cond. cooling | Operator action | Open
…
Millions of data points
Data (process) mining, machine (deep) learning…
Something useful ?
Big data and ML can support the alarm management?
Notes: To solve these ambitious problems we have to answer to the most important question, ….
Does BD and ML can …?
We started this work three years ago … we developed … and we have received strong support from MOL
The log file has a similar structure …
Start and end of an event that can be alarm, warning, operator action …
…

## Slide 7
DATA Warehouse
Target Data
Transformed Data
Patterns and
Rules
01
02
03
05
04
Selection &
cleaning
Transforma-tion
Data
-mining
Evaluation
Integration
Utilisation of the knowlege
monitoring of alarm rationalisation projects
grouping alarms
suggest alarm supression rules
fault detection and diagnosis
support and monitor of the operators
Knowledge Discovery can support alarm management

## Slide 8
Prediction:
80 % of the cases
Root cause analysis:
60 % confidence
ALARMS
OPERATOR ACTIONS
Automation
Recommendation
Grouping:
Parent-children
Illustration of the frequent pattern-based concept
Notes: So what is the potential of frequent sequence mining in alarm management?
Let’s have a simple and hopefully, didactic example. Assume a distillation column and a small fouling after the condenser of the column.
In the simplest case, if two alarms frequently occur together, they can be grouped in order to reduce the operator workload and define more informative process alarms.
Observing a frequent outcome of a sequence, we can make a prediction of the next occurring event and assign an appropriate probability measure as well.
If we have a historic database of the malfunctions, we can realise that the fouling is followed by the recorded sequence, hence we can make a root cause analysis.
On the other hand, we cannot just analyse alarm messages, as the operators constantly interact in the process and change the ongoing processes. In the case of the fouling, they can increase the pump or the cooling efficiency at the condenser. If these solutions does not work, they can reduce the inflow of the whole column, or in the worst case scenario they need to put the appropriate part on a bypass.
So the concept is …
F – flow, p – pressure, T – temperature, Q – heat, A – analysis (prod. quality)
H – high, L - low

## Slide 9
Data warehouse
00
Offline data
Sequence mining
02
Visualisation
01
Online data
03
Deep learning
Matplotlib, plotly, bokeh
spmf toolbox
Keras, TensorFlow
Trained model
Extracted knowledge
Root cause analysis
Seq2seq
Event prediction
Anomaly detection
Online applications
The method and the framework Open source machine learning tools are applicable in the process industry
Notes: We developed these tools as part of our research work with the hope as the concept will work
But know we are just turing it into product, namely to plugins of a SCADA system developed for
water production, treatment and distribution companies.
The main takeaway is that ML can be implemented …
The main prolem is how you can turn the bussiness problem into data analyis task,
how you transform your data …
How you find the good algorithm and most importantly, how the resulted data-driven models
are utilised and MAINTANED.

## Slide 10
DCS
Filtered Database
json
Data processing
AI Framework
EXE packages
1
Business problem
2
Proof of Concept
3
Define requirements
4
Use-cases
5
GUI and integration
6
Test
The process flow of development

## Slide 11
134 station object
35611 variables
7165 trend variables
4 909 701 events
2 531 019 daily archive data
(since 2017 january)
http://www.controlsoft.hu/hu
Water production & distribution

## Slide 12
webSCADA before/after

## Slide 13
KPIs of operation actions
Rare events?
Recommendation system
Future
Improvement
Visualisation
Advanced techniques
Fully integrated
Open source
Realization
Solution
Sequence mining
Event prediction
Prediction
Problem
The related ML task
The python script-based solutions are well integrable
Conclusion

## Slide 14
Rabbit Miner Ltd. offers comprehensive data mining and process systems engineering services. We are specialized in process optimization, data science applications, supply chain management, and Industry 4.0 solutions. Our potential partners and customers are the industrial companies open to new data-driven optimization techniques. Our experience in data science as well as in process systems engineering makes us the ideal innovation and R&D service partner to solve your process optimization problems.
Data-driven process development
Smart monitoring system
Root cause analyses
Decision support
based on process simulation
Rabbit Miner – The process systems engineers