## Slide 1
Theoretical advances in the
NAPLIFE
project
Margaret Island Symposium 20223 on Particles and Plasmas
Laszlo P. Csernai, for the NAPLIFE Collaboration Univ. of Bergen, Norway
Budapest, June 9, 2023
Ensana
Margaret
Island Thermal Hotel,
Margaret Island,
1007 Budapest,
Hungary

## Slide 2
NAPLIFE Collaboration – Participants - ELKH, National Res. Lab.
Laszlo P. Csernai, Tamás S. Biró, Norbert Kroó, Peter J. Lévai, Márk Aladi, Roman Holomb, Miklós Kedves, Archana Kumari, István Papp, Péter Petrik, Béla Ráczkevi, István Rigó, Miklós Veres, Anett Szeledi, Ágnes Nagyné Szokol; Gábor Galbács, Balázs Bánhelyi, Mária Csete, Attila Czirják, Olivér Antal Fekete, Péter Földi, Emese Tóth, András Szenes, Dávid Vass; Attila Bonyár, Nour Jalal Abdulameer, Judit Kámán, Alexandra Borók; Zsolt Fogarassy, Kolos Molnár, Roman Holomb, Péter Dombi, Melinda Szalóki, Laura Juhász; Horst Stoecker, Leonid Satarov, Johann Rafelski, Anton Motornenko; Larissa Bravina, Evgeny E. Zabrodin; Igor N. Mishustin, Daniel D. Strottman, Csaba Tóth, Shereen Zangana, Konstantin Zhukovsky (~> 40)

## Slide 3
Rayleigh-Taylor Instability

## Slide 4
[Clark et al., Phys. Plasmas,
22, 022703 (2015).]
Snapshots of 3D simulation
22.53ns: peak impl. Velocity
23.83ns: bang, max compr.
22.96ns: jet out, up left Green surface: Ablator/DT-f. Peaks: Ablator defects
Colours: Left: fluid speed Right: matter density
~adiabatic compression  80 μm & heating

## Slide 5
NIF – RT instability
The target is compressed to density
~ 700 g/cm3.
But, although an ablator layer is used, only ~ 10%-of the target is ignited.
Elsewhere
the surface protruded as “potato from the potato press”:
RT- instability.

## Slide 6
How can we prevent it Idea - #1

## Slide 7
[ L. P. Csernai, Zh. Eksp. Teor. Fiz. 92, 379-386 (1987) & Sov. Phys. JETP 65, 216-220 (1987) ]
corrected the work of [ A. Taub, Phys. Rev. 74, 328 (1948) ]
λα λα = ± 1
+1
-1

## Slide 8
[ Stefan Floerchinger, and Urs Achim Wiedemann,
Phys. Rev. C 89, 034914 (2014) ]
Light cone
@ CERN in High energy heavy ion collisions

## Slide 9
Fusion reaction: D + T  n(14.1 MeV) + 4He (3.5 MeV)
Constant absorptivity,
Spherical irradiation
Ignition temperature = T1 
Simultaneous, volume ignition up to
0.5 R (i.e. 12% of the volume).
Not too good, but better than:
[ L.P. Csernai & D.D. Strottman,
Laser and Particle Beams 33, 279 (2015).]

## Slide 10
How can we realize it Idea - #2

## Slide 11
… and 35th Hirschegg Int. Workshop on High Energy Density Physics, Jan. 25‐30, 2015
LPB, 36(2), (2018) 171-178.

## Slide 12
Golden Nano-Shells – Resonant Light Absorption

## Slide 13
The absorption coefficient is linearly changing with the radius: In the center, r = 0, αK = 30 cm-1 while at the outside edge αK = 8 cm-1.
The temperature is measured in units of T1 = 272 keV, and Tn = n T1.
Simultaneous, volume ignition is up to 0.9 R, so 73% of the fuel target!
T (MeV)
L.P. Csernai, N. Kroo, I. Papp [ Patent # P1700278/3 ]

## Slide 14
How can we realize it simpler and with less expense

## Slide 15
Thick coin like flat target & Two beams only
X
Thickness of the target is: h … .
h depends on pulse energy, ignition energy, target mass, …
[ Csernai et al., (NAPLIFE Collaboration) Phys. of Wave Phenomena, 28 (3), 187-199 (2020). ]

## Slide 16
However, - no simultaneous ignition, and - no nano-antennas up to now !

## Slide 17
Without nano antennas
The deposited energy from laser irradiation from one side only. The absorption is constant, this leads to an exponentially decreasing energy deposition, and only a negligibly small energy reaches the opposite end of the target.

## Slide 18
With nano antennas
The deposited energy from laser irradiation from one side only. The absorption is modified by nano antennas so that the absorptivity is increasing towards the middle, so that the deposited energy is constant up to the middle. Then the absorptivity is decreasing, but hardly any energy is left in the irradiation front. Thus again only a negligibly small energy reaches the opposite end of the target.
The absorptivity is increased towards the center, due to the implanted nano antennas.

## Slide 19
With nano antennas
Ignition energy is: Qi /m e.g. for DT target: Qi /m = 27 kJ/g  if we have Q = 100 J , then
we can have a target mass:
mDT = Q / Qi g = 3.703 mg.
Then with mDT and ρDT given we get the DT-target’s volume, VDT and hDT = 2.67 mm .
Irradiation from both sides.

## Slide 20
With nano antennas
Ignition is reached at contour line Q = 1.
[ Csernai et al., (NAPLIFE Collaboration) Phys. of Wave Phenomena, 28 (3), 187-199 (2020). ]
Simultaneous ignition in the whole target volume  Short Pulse: ELI - ALPS

## Slide 21
Validation tests at lower energies idea #2 increased absorption via nano-antennas

## Slide 22
Wigner RCP, Budapest
Ti:Sa Hidra Laser: 30mJ, 10Hz, 40fs [P. Racz et al., Wigner RCP]

## Slide 23
Target Modeling and Manufacturing
 Attila Bonyár’s talk

## Slide 24
Transmission Electron-microscopy photos of 75x25 nm gold nano-rod antennas
[Judit Kámán, A. Bonyár et al. (NAPLIFE Collab.)., Gold nanorods …, 10th ICNFP 2021, Kolymbari]

## Slide 25
TEM Photo of ~uniformly implanted nanorod antennas in UDMA target polymer. The density is 9-20 / μm3 [Judit Kámán, A. Bonyár et al. (NAPLIFE Collab.)., Gold nanorods …, 10th ICNFP 2021, Kolymbari, Crete, Greece, 30 August 2021.]

## Slide 26
Nano-particle absorption
1 ps laser pulse length, λ = 800 nm, one-sided & two-sided irradiation tested,
85-100 % absorption in the target length h. Nano-antenna shapes, layer configurations, layer distribution varied & analyzed.
[M. Csete, et al., U. Szeged, HU https://doi.org/10.1007/s11468-021-01571-x 10.3103/S1541308X20030048 ]
The target absorptivity is increased via core-shell type plasmonic nano-shells. Calculations via solving the Maxwell equations, and evaluating the ohmic heating were performed using the COMSOL simulation package.

## Slide 27
Layered target with variable light absorption
Representative uniform & Gaussian
number density distributions of (d) 70 oriented nanorods, in a 1 × 1 × 21 µm3 supercell of UDMA polymer target, with random location distribution.
[ M. Csete, A. Szenes, E. Tóth, D. Vass, O. Fekete, B. Bánhelyi, T. S. Bíró, L. P. Csernai, N. Kroó:
„Comparative study on the uniform energy deposition achievable
via optimized plasmonic nanoresonator distributions“,
Plasmonics (2022), 17: 775-787; https://doi.org/10.1007/s11468-021-01571-x. ]

## Slide 28
Validation tests at lower energies idea #1 Simultaneous (time-like) transition (ignition)
 Two opposing beams

## Slide 29
Validation tests – Target manufacturing
Two basic principles are tested on non-fusion material targets at low energies
Implanted with nano-antennas  Amplified absorption √
Multilayer targets  Simultaneous Ignition (in progress)
[M. Csete, A. Bonyár,
I. Papp, P. Rácz, et al.] In preparation

## Slide 30
Multilayered fuel target

## Slide 31
Laser Wake Field Collider
Ǝ Pre-compression/acceleration, before ignition
Ion (e.g. p) Energy Ep ≈ 50 MeV (or more)
Initial beam densities assumed: nH ≈ γ n0 = 2·10-19/cm3 and 2·10-21/cm3
≈ nliquid-H , ≈ nNIF /1000 (/wo precompression!)
Target density after interpenetration: nt ≥ 2 nH
The ionization of the H atoms at ignition in a Laser Wake Field (LWF) wave due to the irradiation from both the +/- x directions
[ Papp, I., et al., NAPLIFE, Phys. Lett. A 396, 12724 (2021). ]

## Slide 32
Validation tests  Laser Induced Fusion
with Nanoantennas

## Slide 33
Deuterium production ( PRELIMINARY ! )
H
H
D
5-12% D + 88-95% H 100% H ~ 1017 D / pulse (10Hz) Balmer-α line
Two step process (average of 20 shots):
p + e*  n + ν \ electron capture (-1.24 MeV)
n + p  d + γ \ neutron capture (+2.22 MeV)
Electron capture may happen spontaneously in heavy nuclei, here laser light and resonant nanorods act similarly, high e density
UDMA (470: H38, C23, O8, N2)
(N.K.*)

## Slide 34
Deuterium production w ith 795nm 40fs Ti:Sa laser 1016-1017 W/cm2 intensity
UDMA-TEGDMA target 20-100 μm thick, \w & \wo Au nanorods 25x85nm.  5 mJ pulse -> crater of 4.55-1.07·1014 μm3 \w &\wo Au ~ 15/ μm3
 From the crater the emitted matter was analysed by Raman spectroscopy & Laser Induced Breakdown Spectroscopy (LIBS).
(N.K.*)

## Slide 36
( 2022 )

## Slide 37
With Nanorods (Au2) at 25 mJ laser pulse
~4 times increased D production, compared to 1 mJ pulse

## Slide 38
( 2022 )

## Slide 39
25x130 nm antennas, resonant for λ=795 nm
[L. Novotny (2007)]
Initial 2 ord. magn.
“Final.

## Slide 41
Resilience of Nanorod Antenna with COMSOL
Good qualitative agreement between FEM and EPOCH/PIC methods Quantitative difference: the hydrodynamic model of the electron plasma (FEM) predicts a sharper resonance than the kinetic model (EPOCH/PIC)
FEM computations with the same model parameters [M.Csete et al.]

## Slide 42
( 2023 )

## Slide 43
Accumulated momentum of conduction electrons in vacuum (blue) and in UDMA (black)
25x85 nm antennas, resonant for λ=795 nm in UDMA polymer
[L. Novotny (2007)]

## Slide 44
( 2022 )

## Slide 45
Puzzle ?

## Slide 47
Theoretical studies in progress =>
We pursue kinetic model (EPOCH) studies in the same Calculational Box, where the nano-rod antenna is surrounded be hydrogen target.
W assume that the hydrogen is relatively dense and ionized, in order to study what effect will have the nano-rod antennas on the surrounding protons.
Idea #3

## Slide 48
Laser
I = 4 ∙ 1017 W/cm2 V ~ 7.1 ∙ 1012 V/m
I = 4 ∙ 1015 W/cm2 V ~ 2.6 ∙ 1012 V/m

## Slide 49
I = 4 ∙ 1017 W/cm2 dV ~ 8 ∙ 1012 V/m
Dipole L = 85 nm
LHC dV ~ 1 ∙ 106 V/m
Dipole L ~ 16 cm
Neighboring protons are accelerated (100-200 nm)

## Slide 50
Laser wake field acceleration mechanism =>
BUT Proton amplitudes
& speeds are smaller

## Slide 51
Number of 1-2 MeV protons is about 1-100
=>
About 3 ordrs of magnitude less than electrons => small number of Deuterium

## Slide 52
 IDEA # 3: New fusion mechanism
Traditionally (NIF) after ignition, DT burning is spreading by alpha particle self heating. This turns out to be slower than expansion after extreme compression and extreme pressure.
HINT: Here after simultaneous (time-like) ignition attraction of large number of electrons collectively accelerate protons, which can induce nuclear reaction (e.g. transmutation).
We try to verify this mechanism and evaluate if the rate that can be achieved this way is sufficient for massive energy production

## Slide 53
Thanks for your attention