## Slide 1
HIGH FIELD PLASMONICS AND SOME APPLICATIONS
NORBERT KROO
(on behalf of the NAPLIFE Programme)
WIGNER PHYSICS RESEARCH CENTER and
HUNGARIAN ACADEMY OF SCIENCES
PP2023, 06.09.2023

## Slide 2
THE OPTICAL NEAR FIELD

## Slide 3
Ti:Sa laser: ʎ=800nm (~1.55eV) ; t(SPP)~30fs
SPP
LSPP
PLASMONICS AND HIGH FIELDS APPLICATIONS
Special type of the optical near field. No diffraction limit.
ω(eV)

## Slide 4
Light gets through the holes much smaller, than the wavelength of applied light.
MOST OF THE ENERGY IS CONCENTRATED AT THE SURFACE: GIANT FIELD ENHANCEMENT!
VACUUM
METAL

## Slide 5
LOCALIZED PLASMONS (SPP andLSPP) UP TO 10²⁰ W/cm²)
(The basic difference between SPP-s and LSPP-s)
LSPP: - NO EM FIELD PENETRATION INTO THE PLASMONIC MATERIAL (e.g. metal)
- SMALLER PENETRATION INTO THE DIELECTRIC /VACUUM
-NO DISPERSION
-BROADER RESONANCE

## Slide 6
LSPP

## Slide 7: PLASMON RESONANCE OF NANOPARTICLES SHAPE AND SIZE DEPENDENT!
Sphere
Bulk
Nanoshell:
a
b
Hole
Nanoshell plasmon resonance depends on the x ratio .
Surface

## Slide 8
SPP and LSPP are a „NEW TYPE OF LIGHT”, they are
1. BOUND TO THE (METAL) SURFACE (SPP and LSPP)
2. HAVE SPECIFIC DISPERSION PROPERTIES (LSPP no dispersion)
3.THE DIFFRACTION LIMIT DOES NOT APPLY,
4.CAN BE SQUEEZED TO NANOSIZED VOLUMES
5. COULD REPRESENT VERY HIGH ELECTRIC FIELDS (hot spots)
6. SCREEN POSITIVE (e.g.proton) PARTICLE CHARGES
7. IS CORRELATED MOTION OF A HIGH NUMBER OF CONDUCTION
ELECTRONS
8. MAY BE THE SOURCE OF DIFFERENT NONLINEAR PROCESSES
9.SHOW NON-CLASSICAL PROPERTIES

## Slide 9
DEVELOPMENT OF HIGH INTENSITY SHORT PULSE LASERS IN TIME

## Slide 10
we

## Slide 11
PLASMA MIRROR REFLECTIVITY
Ch.Ziener at al : J.Appl.Phys. 93,768 (2013)

## Slide 12
Non doped (amplification: 30x)
Doped (amplification: 40x)
~10¹¹/cmᶾ gold nanoparticles
Laser
Thickness: ~30μ or 160μ
Focus: 20μ diameter
Pulse length: ~40fs
Intensity: max. ~4.10¹⁷W/cm²
LIGHT NOT REFLECTED, GOLD NANOPARTICLES REACHED!

## Slide 13
~10¹⁴ W.cm ̄²
Laser pulse length: 300 fs
Ti:Sa laser: ʎ=800nm, ~1.55eV
30μ
40μ
Giant plasmonic amplification; the laserlight reaches the nanoantennas;
Spot size nearly constant

## Slide 14
Checcotti

## Slide 15
PLASMAMIRROR
PENETRATION
3.10¹⁷W/cm²
REFLECTIVITY OF A POLYMER FILM WITH AND WITHOUT RESONANT GOLD NANORODS

## Slide 16
Chart: Longitudinal position [mm]
| 3.6 | 3.6 | 3.4 | 3.2 | 3 | 2.8 | 2.6 | 2.4 | 2.2000000000000002 | 2 | 1.8 | 1.6 | 1.4 | 1.2 | 1 | 0.6 | 0.4 | 0.2 | 0 | 0 | -0.2 | -0.4 | -0.6 | -0.8 | -1 | -1.2 | -1.4 | -1.4 | -1.6
Volume Au2 - 10 mJ | 95250.9997 | 96412.5951 | 84604.3971 | 75419.9867 | 101118.1905 | 85074.2044 | 84343.0544 | 72965.3383 | 52681.584 | 56078.2645 | 49107.967 | 44054.0456 | 55422.8732 | 107902.4535 | 81869.3538 | 40089.1545 | 30865.173 | 32390.752 | 41080.8234 | 40356.2222 | 50275.0579 | 56164.0722 | 67908.6305 | 75215.5697 | 85022.5776 | 99452.937 | 105115.5811 | 105135.5948 | 121388.9403
Volume Au2 - 25 mJ | 171796.1935 | 77927.0397 | 77317.6986 | 322204.1442 | 524509.451 | 367102.8715 | 381845.7952 | 163521.643 | 108193.0954 | 90780.4479 | 84447.4949 | 77988.3685 | 85079.5249 | 92261.1921 | 102338.1659 | 89308.4281 | 94785.608 | 72368.2911 | 85196.9421 | 93173.6331 | 125389.8206 | 473151.6989 | 458566.0215 | 343329.69 | 239761.3744 | 129269.2734 | 118171.6763 | 142357.8027 | 111276.5142 | 112844.0347 | 161534.9375
3,2.10¹⁷W/cm²
2,2.10¹⁷W/cm²
1,2.10¹⁷W/cm²
0,5.10¹⁷W/cm²
Chart: Longitudinal position [mm]
| 0 | 0 | 0.2 | 0.6 | 0.6 | 0.8 | 0.6 | 0.4 | 0.2 | 0 | -0.2 | -0.2 | -0.4 | -0.6 | -0.8 | -0.6 | -0.4 | -0.2 | 0 | 0.2 | 0.4 | 0.6 | 0.6 | 0.8 | 1 | 1.2 | 1.4 | 1.4 | 1.6 | 1.8 | 2.6
Volume - Au2 - 25 mJ | 171796.1935 | 77927.0397 | 77317.6986 | 322204.1442 | 524509.451 | 367102.8715 | 381845.7952 | 163521.643 | 108193.0954 | 90780.4479 | 84447.4949 | 77988.3685 | 85079.5249 | 92261.1921 | 102338.1659 | 89308.4281 | 94785.608 | 72368.2911 | 85196.9421 | 93173.6331 | 125389.8206 | 473151.6989 | 458566.0215 | 343329.69 | 239761.3744 | 129269.2734 | 118171.6763 | 142357.8027 | 111276.5142 | 112844.0347 | 161534.9375
Volume - Au0 - 27,7 mJ | 160946.9652 | 142535.4683 | 128882.9043 | 114670.3694 | 92810.559 | 76026.8821 | 69164.4553 | 70659.7141 | 66100.6033 | 57342.2355 | 49468.179 | 43929.63 | 46265.5601 | 66359.7642 | 112720.194 | 142992.3673 | 74496.5466 | 86969.5341 | 92720.0729 | 105941.9971 | 115066.9048 | 134806.2899 | 157088.4402 | 163777.4392 | 178881.1504 | 191782.9598
HIGH FIELD PLASMONICS WORKS!
CRATER VOLUMES

## Slide 17
LINEAR

## Slide 18
Matter under extreme conditions
(extremely high intensities)
I = 1016 W cm-2
E ~ 109 V/cm
Rapid ionization of valence electrons
Tunnelling
1014 - 1015 W cm-2
Over the barrier
> 1015 W cm-2
Each atom loses at least one electron. Some can lose as many as 6 !
single
atom
+
High intensity
Photoeletric Effect
No1 appl.

## Slide 19
slope: 4.3 ± 0.4
Multiphoton tunneling
transition at
~4x1010 W/cm2 incident
intensity,
~5.5x108 V/m field
Keldysh-gamma =31
→ indication of well-known
field enhancement of surface
plasmonic fields
slope: 0.89 ± 0.03
Tunneling from ~4x1010 W/cm2
W: work function, El: laser field strength
MULTIPHOTON ELECTRON EMISSION FROM GOLD
PLASMONIC ENHANCEMENT!

## Slide 20
From multi plasmon electron emission
Kisérleti tapasztalat ~10¹² W/cm²-ig
Born-Openheimer?: >10¹⁵ W/cm²; Relativistic phenomena: >10¹⁸W/cm²
MAY PLASMONS EXIST IN THESE LASER INTENSITY REGION?

## Slide 21
Transverse and longitudinal modes!

## Slide 22
Ti:Sa laser

## Slide 23
Ti:Sa LASER SPECTRA AT DIFFERENT PULSE ENERGIES

## Slide 24
ILLUSTRATION OF THE RESULT OF THE SCREENING EFFECT
A.Y.Wong and C-C.Shinh:UCLA 2019
Illustration with the H+B
3He reaction
Ponderomotive screening Fᵨ = (e²/4mₑꙍ²).grad (E²)

## Slide 25
Demonstration of the correlated state

## Slide 26
Some potential new energy technologies
(involving nanotechnologies)
P3HT Cell efficiency = 6%
SPESC (P3HT) efficiency = 17.5%
Toward our proposal
?

## Slide 27
E = mc²
Laserbeams
The most succesful technologies imitate nature
No2 application (LSPP)

## Slide 28
Long laser pulses (~50ns)
Raileigh-Taylor instability
Complicated target construction
Enormous laser energy (400/1.8MJ)
1sho
TO COMBINE 2 DIFFERENT (e.g. fusion and nano-) TECHNOLOGIES TO REACH FUSION AT THESE ULTRAHIGH EM FIELDS?
10⁵USD

## Slide 29
SOME POTENTIAL EXPLOITABLE HIGH FIELD PLASMONIC PROCESSES:
1.Go for localized surface plasmon polaritons (LSPP)
2.Lifetime of LSPP-s is in the few ten femtosecond timerange. We may get high
intensity laser pulses in this timediapazon and the plasma instabilities disappear.
3.High electron densities and EM fields can be obtained in small (nanosized) volumes on
resonant plasmonic nanoparticles (hot spots).
4.The near field of plasmons screen the repulsive field of positively charged (e.g. protons)
particles and they may fuse more easily.
5.The large number of conduction electrons move in plasmonic excitations in correlated
way and their momentum may be transfered in high exciting fields to positive particles
moving together with them, further increasing the probability of nuclear fusion.
6.With these short pulses we do not need many beams, like in the NIF, the target can be a
thin film, illuminated only by 2 beams from opposite directions, reaching the same
energy density in the whole thicknes of the target sample, and this may lead to
timelike fusion.
OUR PROPOSAL: COMBINE PLASMONICS WITH NUCLEAR FUSION TECHNOLOGY

## Slide 30
OUR GOAL IS:
To explore these properties of LSPP-s with the intention to
-drive for nanoplasmonic aneutronic fusion reactions,
-and this way scale down the size and costs of laser based nuclear fusion
facilities;
-find solutions at lower optimal laser intensities;
When the winds of changes are blowing some build shelters, but some others build wind turbines

## Slide 31
FEMTOSECOND LASER PULSES
HIGH REPETITION FREQUENCY
LIGHT SPEED: NO TIME FOR INSTABILITIES,ONLY TWO BEAMS,
VOLUME IGNITION
d ~ n.10μ
NANOPARTICLES IN THE FUSION MATERIAL
NANOSHELLS
(nx10nm)
NANOROD (~85x25nm)
ʎ = 800nm
Resonant
n.10μ
Here only indications. Details in other talks, both in theory and experiments.

## Slide 32
Two-sided irradiation

## Slide 33
1. DIAGNOZIS (crater volume)
40μ
Volume max. 3.5V₀
Volume:V₀
Laser shots from one side of a thick (~160μ) foil

## Slide 35
SEM IMAGE OF UDMA WITH AU NANORODS SEM IMAGE OF UDMA WITHOUT AU NANORODS
Images at 17.5mJ laser energy, 1,16.10¹⁷ W/cm² laser intensity.The volume of the crater of the sample with nanorods (b) is 1.98 times that of the sample without rods (a).
and Zygo images of the same craters
a
b

## Slide 36
Au1
Au2
AuX

## Slide 37
Chart: Surface roughness as function of the longitudinal position of the Au2 vs. Au0 samples Energy of the impulse: 27,7 mJ (Au0) and 25 mJ (Au2)
| 0 | 0 | 0.2 | 0.6 | 0.6 | 0.8 | 0.6 | 0.4 | 0.2 | 0 | -0.2 | -0.2 | -0.4 | -0.6 | -0.8 | -0.6 | -0.4 | -0.2 | 0 | 0.2 | 0.4 | 0.6 | 0.6 | 0.8 | 1 | 1.2 | 1.4 | 1.4 | 1.6 | 1.8 | 2.6
Sa - Au2 - 25 mJ | 2.16 | 2.116 | 2.834 | 6.704 | 8.57 | 7.002 | 7.469 | 4.093 | 3.701 | 2.366 | 1.616 | 1.448 | 1.039 | 0.88 | 0.733 | 0.862 | 1.2 | 1.252 | 2.166 | 2.946 | 4.246 | 9.27 | 8.801 | 6.177 | 4.688 | 2.56 | 2.219 | 2.417 | 1.797 | 1.263 | 0.58
Sa - Au0 - 27,7 mJ | 0.555 | 0.629 | 0.668 | 0.749 | 0.814 | 1.064 | 0.984 | 0.98 | 1.106 | 1.173 | 1.344 | 1.409 | 1.572 | 1.72 | 2.818 | 3.524 | 1.372 | 1.273 | 0.939 | 0.816 | 0.762 | 0.719 | 0.66 | 0.583 | 0.569 | 0.552
3,2.10¹⁷W/cm²
1,2.10¹⁷W/cm²
0,5.10¹⁷W/cm²
2,2.10¹⁷W/cm²

## Slide 38
Ilaser > 10¹⁶ W/cm²
2.Diagnozis :Raman scattering from the crater surface
a
b
arXiv2210.00619(2022),submitted to Advanced Optical Materials
Au0
Au1
Au2

## Slide 39
IN WORK BUT NOT YET CONCLUDING TECHNIQUES:
1.Atomic optical spectroscopy,
2. Mass spectrometry.
3.Nuclear detection techniques.
3: CR39 film, 1 laser shot
1
2

## Slide 40
THE PROBLEMS WE ARE FACING TODAY CAN NOT BE SOLVED WITH THE SAME WAY OF THINKING BY WHICH WE CREATED THEM.
THE ADVICE OF ALBERT EINSTEIN FOR THE FUTURE:
THIS IS WHY CREATIVE SCIENTIFIC THINKING IS THE KEY TO OUR FUTURE
THANKS FOR YOUR ATTENTION