## Slide 1: Results and Experiences from LUMI running CFD workloads
István Reguly, PPCU ITK
reguly.istvan@itk.ppke.hu
GPU Day 2023

## Slide 2: AMD MI250X GPUs & LUMI
Two graphic compute dies (GCDs)
64GB of HBM2e memory per GCD (total 128GB)
26.5 double TFLOPS peak performance per GCD
1.6 TB/s peak memory bandwidth per GCD
110 CU per GCD, totally 220 CU per GPU
The interconnect is attached to the GPU (not to the CPU) – 200 Gb/s each
LUMI-G: 2560 nodes, each with 4 MI250X (8 GCD)
  1 64-core AMD Trento CPU
  375 PFLOP/s

## Slide 3: Programming LUMI/AMD GPUs
Programmability is a challenge for AMD
  OpenCL did not gain enough traction in HPC
HIP: “CUDA clone” – trivial portability for many codes
  Except new features
  Libraries still an issue
  ROCm stack comes with HIP
OpenMP offload
  Cray compilers
  AOMP
SYCL
  Intel’s DPC++ extended to support AMD GPUs
  hipSYCL aka. OpenSYCL
Fortran?
  HIP API bindings, but kernel in C/C++
  OpenMP offload
    Cray support OK
    AOMP based on flang, very immature

## Slide 4: Application Development with OPS/OP2
SYCL
MPI
OpenACC
Source-to-Source translator (Python)
OP2 Platform Specific Optimized Backend libraries
Conventional Compiler (e.g. icc, nvcc, pgcc, clang, XL, Cray, dpcpp) + compiler flags
Hardware
Link
OpenMP and OpenMP4.0
Application
OPS/OP2 Application (Fortran/C/C++ API)
Modified Platform Specific
OPS/OP2 Application
Platform Specific Optimized Application Files
Mesh
(hdf5)
Platform Specific
Binary Executable
CUDA
SIMD Vectorized
Sequential
Human
Readable
+
Well Formatted

## Slide 5: Structured-mesh stencil codes
Boilerplate generated by OPS
  Pure MPI, MPI+OpenMP, MPI+SYCL (CUDA/HIP/OpenCL/OpenACC)
CloverLeaf 2D/3D – 7680^2, 408^3
  Hydrodynamics code from AWE, part of Mantevo suite
  ~100 nested loops, ~35 doubles per grid point, lots of small boundary loops
OpenSBLI – Shock Boundary Layer Interactions - 320^3
  Finite Difference Navier-Stokes solver with shock capturing from Univ of Southampton
  High-level pyhton interface, generates OPS
  Two versions – Store All (SA) or Store None (SN) – how much recompute for derivatives
Acoustic solver – 320^3
  8th order finite differences
  Very costly MPI halo exchanges
  Two variants

## Slide 6: Unstructured mesh codes
MG-CFD
  Multigrid enabled Euler equations solvers
  Representative of production workloads at Rolls-Royce
  NASA Rotor37 testcase with 8M cells
  Rig250 – DLR 650M cell mesh
Variants:
  “Global coloring” – 1 level of coloring, poor locality
  “Hierarchical coloring” – 2 levels of coloring, good locality within blocks
  “Atomics”
Global coloring
Hierarchical coloring

## Slide 7: Single GPU – Structured mesh
Chart: Runtime (seconds)
| CloverLeaf | CloverLeaf 3D | RTM | OpenSBLI SN | OpenSBLI SA | SO 08
HIP | 4.6028 | 11.679 | 1.7489 | 13.0362 | 10.3504 | 4.2598
Cray OMP | 4.9189 | 2.0403 | 15.2976 | 10.3929 | 5.2975
AOMP | 8.9879 | 25.5535 | 2.1413 | 10.7986 | 5.4013
DPCPP ndrange | 5.5338 | 14.1613 | 1.896 | 14.7647 | 12.3913 | 4.7931
DPCPP flat | 59.3909 | 15.0127 | 2.1578 | 16.3838 | 11.8893 | 6.5998
OpenSYCL ndrange | 4.8725 | 13.0301 | 1.5841 | 14.5303 | 11.2922 | 4.2016
OpenSYCL flat | 6.3581 | 13.0422 | 3.322 | 14.5415 | 18.6339 | 21.9772
3.83 | 7.78 | 1.05 | 6.72 | 6.58 | 14.10
A100:
Notes: HIP always best, except acoustic problems
OpenMP – cray failed with 1 app, AOMP with another. Cray when works, is reasonably good, AOMP not great
SYCL – flat “should” guess reasonable block size, nd_range we have to. Nd_range is close to HIP, OpenSYCL consistently better than DPC++

## Slide 8: Quick detour: SYCL loop formulations
Anew(0,0) = 0.25f *
( A(1,0) + A(-1,0)
+ A(0,-1) + A(0,1));
Queue.submit([&](cl::sycl::handler &cgh) { ...//Accessors cgh.parallel_for<class apply_stencil>( cl::sycl::range<2>(jmax, imax), [=](cl::sycl::item<2> idx) { ...//Views, bounds checking
Anew(0,0) = 0.25f *
( A(1,0) + A(-1,0)
+ A(0,-1) + A(0,1));
Queue.submit([&](cl::sycl::handler &cgh) { ...//Accessors cgh.parallel_for<class apply_stencil>( cl::sycl::nd_range<2>(
cl::sycl::range<2>(jmax, imax), cl::sycl::range<2>(4, 32)),
[=](cl::sycl::nd_item<2> idx) { ...//Views, bounds checking
“Flat”
“nd_range”

## Slide 9: Achieved throughput
 | Maximum | CloverLeaf 2D | CloverLeaf 3D | Acoustic | OpenSBLI SA | OpenSBLI SN
AMD MI250x GCD | 1320 GB/s | 1001 GB/s | 738 GB/s | 294 GB/s | 657 GB/s | 520 GB/s
NVIDIA A100 | 1386 GB/s | 1203 GB/s | 1108 GB/s | 490 GB/s | 1034 GB/s | 1008 GB/s
NVIDIA H100 | 1840 GB/s | 1556 GB/s | 1423 GB/s | 1288 GB/s | 1532 GB/s | 1383 GB/s

## Slide 10: Workgroup size/shape tuning
Chart: Default vs. tuned workgroup size
| CloverLeaf | CloverLeaf 3D | RTM | OpenSBLI SN | OpenSBLI SA | SO 08
HIP default BS | 4.6521 | 14.0961 | 2.2534 | 14.2988 | 10.3105 | 6.1323
HIP tuned BS | 4.6028 | 11.679 | 1.7489 | 13.0362 | 10.0661 | 4.2598
101% | 121% | 129% | 110% | 102% | 144%

## Slide 11: MG-CFD Rotor 37 8M
Chart: Runtime (s)
| Atomics | Global | Hierarchical
HIP | 1.5381 | 7.2952 | 3.1889
DPCPP | 1.7123 | 7.8744 | 4.1213
OpenSYCL | 2.7265 | 7.4518 | 3.8465
Cray OMP | 2.7082
AOMP | 2.4464
1.430 | 3.450 | 2.783
A100:
0.92 | 2.88 | 2.373
H100:

## Slide 12: Scalability
Strong scaling: max size that fits in single GCD’s 64GB of memory
Weak scaling: as previous benchmarks
Variants:
  Host-copy: halo data gathered on GPU, copied to host, MPI comms are between CPUs
  GPU Direct: MPI buffers are on the GPUs
  GPU Direct + Tiling: fewer but larger MPI messages + redundant compute over halos

## Slide 13: CloverLeaf 2D
Strong scaling efficiency vs. 1 GPU:
  85% to 32 GPUs (2GB working set)
  56% to 128 GPUs (0.5GB working set)
Weak scaling efficiency vs. 2 GPUs: 96% efficiency to 8192 GPUs
Chart: Number of GPUs
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192
Plain | 24.9105 | 13.2964 | 6.8266 | 3.5593 | 1.8974 | 0.99819 | 0.60372 | 0.43205 | 0.33828 | 0.29145 | 0.26683 | 0.25883 | 0.25174 | 0.25238
Direct | 24.9266 | 13.3554 | 6.9179 | 3.589 | 1.882 | 0.94042 | 0.54744 | 0.39159 | 0.29189 | 0.23658 | 0.21975 | 0.21051 | 0.2016 | 0.21538
Tiled + Direct | 24.9112 | 13.1997 | 6.7306 | 3.4982 | 1.8299 | 0.90973 | 0.51442 | 0.34742 | 0.24052 | 0.19517 | 0.17494 | 0.17025 | 0.16718 | 0.18515
Chart: Number of GPUs
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192
Plain | 4.6513 | 4.8531 | 4.896 | 4.9204 | 4.9509 | 4.9823 | 4.9887 | 4.98 | 4.9894 | 4.9979 | 4.9993 | 5.0063 | 4.9999 | 5.0084
Direct | 4.6505 | 4.8888 | 4.973 | 4.9667 | 5.0895 | 5.1001 | 5.0603 | 5.0482 | 5.0688 | 5.0516 | 5.0653 | 5.0688 | 5.0675 | 5.0707
Tiled + Direct | 4.6342 | 4.8151 | 4.819 | 4.796 | 4.8181 | 4.8315 | 4.8426 | 4.8519 | 4.8632 | 4.8707 | 4.8741 | 4.882 | 4.8922 | 4.8934

## Slide 14: CloverLeaf 3D
Strong scaling efficiency vs. 1 GPU: 69% to 32 GPUs, 32% to 128 GPUs
  Lot more communications
  Tiled + Direct hitting handshake size, Direct isn’t?
Weak scaling efficiency vs. 2 GPUs: 90% efficiency to 8192 GPUs
Chart: NUmber of GPUs
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192
Plain | 38.4143 | 19.7256 | 10.2555 | 5.68 | 3.4819 | 2.0964 | 1.3563 | 1.1283 | 0.84954 | 0.70523 | 0.6317 | 0.5906 | 0.58665 | 0.60081
Direct | 38.4238 | 19.1898 | 9.7684 | 5.3251 | 3.1712 | 1.7397 | 1.1017 | 0.93532 | 0.69188 | 0.58446 | 0.52548 | 0.49405 | 0 | 0.52355
Tiled + Direct | 38.3423 | 19.2327 | 9.7908 | 5.1579 | 3.0043 | 1.8337 | 1.1254 | 0.9269 | 0.64948 | 0.50765 | 0.44869 | 0.42042 | 0.38825 | 0.38717
Chart: Number of GPUs
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192
Plain | 11.6163 | 11.6657 | 12.6289 | 13.1702 | 13.1983 | 13.5521 | 13.6782 | 13.7942 | 13.8269 | 13.9362 | 13.97 | 13.9464 | 13.9472 | 13.9411
Direct | 11.6188 | 11.4489 | 12.2056 | 12.3913 | 12.4264 | 12.5174 | 12.6394 | 12.746 | 12.753 | 12.7728 | 12.8089 | 12.7997 | 12.8072 | 12.8137
Tiled + Direct | 11.5626 | 11.5435 | 12.19 | 12.3887 | 12.3039 | 12.8346 | 13.1028 | 13.0076 | 13.2526 | 13.829 | 13.93 | 13.9641 | 14.1184 | 14.2565

## Slide 15: OpenSBLI – StoreNone version
Strong scaling efficiency vs. 1 GPU: 77% to 32 GPUs, 69% to 128 GPUs
Weak scaling efficiency vs. 2 GPUs: 95% efficiency to 8192 GPUs
1.1 Trillion grid points
Chart: Number of GPUs
| 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192
Plain | 13.712 | 6.9817 | 3.8495 | 2.6776 | 1.8184 | 1.0563 | 0.70462 | 0.51492 | 0.41068 | 0.36006 | 0.3499 | 0.38123 | 0.53421
Direct | 13.1491 | 6.256 | 3.2659 | 2.0819 | 1.2166 | 0.60999 | 0.37616 | 0.26259 | 0.2194 | 0.20157 | 0.21566 | 0.27997 | 0.4322
Tiled + Direct | 13.1535 | 6.3537 | 3.1468 | 1.8613 | 0.95548 | 0.52112 | 0.26603 | 0.16604 | 0.11494 | 0.10645 | 0.12625 | 0.15923 | 0.32809
Chart: Number of GPUs
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192
Plain | 12.4166 | 12.9629 | 13.654 | 14.5989 | 15.3106 | 16.3003 | 16.7713 | 16.9551 | 17.0317 | 17.5561 | 17.5789 | 17.6718 | 17.8317 | 17.9775
Direct | 12.4287 | 12.6127 | 12.7583 | 12.9467 | 13.1085 | 13.3378 | 13.5912 | 13.4847 | 13.6268 | 13.9044 | 13.9236 | 13.9676 | 14.0375 | 14.2622
Tiled + Direct | 12.453 | 13.6106 | 13.8027 | 13.4183 | 13.4633 | 13.7697 | 14.0478 | 14.0467 | 14.0391 | 14.3731 | 14.3925 | 14.411 | 14.4898 | 14.6947

## Slide 16: MG-CFD – Rig250 case
Chart: Rig250 h03s
| 16 | 32 | 64 | 128 | 256 | 512 | 1024
PT-Scotch KWAY | 2.8647 | 1.3389 | 0.66426 | 0.36373 | 0.25454 | 0.16175
Ideal | 2.8647 | 1.4323 | 0.71617 | 0.35808 | 0.17904 | 0.089521 | 0.044761
Strong scaling efficiency vs. 16 GPU: 97% to 128 GPUs, 55% to 512 GPUs

## Slide 17: Conclusions
Extended OP2 and OPS to support HIP, OpenMP offload, SYCL
  Various execution strategies for OP2 to avoid data races
Benchmarking Structured & Unstructured mesh codes
  Native HIP still best, but SYCL close enough
  Hardware utilization still not close to NVIDIA…
LUMI supercomputer
  Excellent scalability – NIC per GPU very efficient
  Go, apply for access!
SYCL languate for portability? – not on CPUs…