## Slide 1: High-intensity femtosecond laser irradiation experiments on polymer targets doped with gold nanorods
Márk Aladi, Ádám Inger, Miklós Á. Kedves, B. Ráczkevi
Wigner Research Centre for Physics
NAPLIFE Collaboration

## Slide 2
Introduction
Motivation, purpose
  Detection of plasmonic amplification, e.g. higher energy protons, ions
  Detection of fusion products, e.g. alpha particles, Deuterium
Experiments at Wigner
  LIBS (laser induced breakdown spectroscopy), MS (mass spectrometry)
  Reflection/transmission measurements
  Study of the effect of the laser contrast
Measurements at the ELI-ALPS laser facility (in cooperation with NLTL group from the Univerity of Szeged)
  Thomson Parabola Spectrometer
  Nuclear trace detectors
  Nuclear particle detectors (by colleagues from ATOMKI)
Preliminary results
Conclusions, further plans (Márk Aladi’s talk)

## Slide 3
Reflection/transmission measurements at Wigner RCP
Arrangement Results

## Slide 4
Laser contrast studies at Wigner RCP
Parameters of the Coherent Hidra laser at Wigner RCP laser plasma laboratory
Maximum pulse energy: 30 mJ
Minimum pulse duration: 40 fs
Central wavelength: ~800 nm
Repetition rate: 10 Hz
Beam diameter (1/e2): 15 mm
Contrast (ns): 106 with pulse slicer (no specification for ps contrast)
Recent measurements with a photodiode:
prepulse at -2.8 ns

## Slide 5
Contrast measurements with our new 3rd order autocorrelator
Prepulse at -2.8 ns with original setting and after the optimization of the pulse slicer delay
3rd order autocorrelation signals full and ps range

## Slide 6
Plasma plume with prepulse
Maxwell-Boltzmann fit:
v = 9∙104 m/s
and without prepulse
v = 1.1∙105 m/s

## Slide 7
Measurements at the ELI-ALPS laser facility
Laser irradiation of the targets, detection of particles by:
- Thomson Parabola Spectrometer (TPS), in cooperation with Károly Osvay’s group of NLTL lab at the University of Szeged
- CR-39 trace detector plates
- scintillation detectors for neutron (and X-ray/gamma)
(by Barna Biró and László Stuhl from ATOMKI , Institute for Nuclear Research))
Laser: Sylos Experiment Alignment parameters:
- max energy ~ 40 mJ from the laser, 70-80% on the target surface
- wavelength centre 825 nm, typical spectrum 750 – 960 nm
- min pulse length 12 fs, longer pulses with negative chirp
focused beam size min ~ 3 μm
Contrast 1010

## Slide 8
Thomson Parabola Spectrometer
(Master Thesis of Nils Schroeter, 2017)

## Slide 9
Experimental system of the NLTL Group of the University of Szeged
(K. Osvay and coworkers)

## Slide 10
Target types used in the experiments:
UDMA-TEGDMA
UDMA-MMA, deuterated (D100)
UDMA-TEGDMA with BN
All 3 types:
  Au0: without gold nanorods
  Au2_RE: with gold nanorods of resonant size (25 x 85 nm)
  Au2_NR: with gold nanorods of non-resonant size (25 x 34 nm)
Thicknesses: 150 or 400 μm
Targets

## Slide 11
Pictures of the targets and holders

## Slide 12
Target inspection during the irradiation
#4 Au2-400
BN-APTES-Au2_NR

## Slide 13
Photos of the experimental set-up

## Slide 16
Thomson Parabola Spectrometer MCP

## Slide 17
Exposure of CR-39 trace detector plates

## Slide 18
Scintillation detectors

## Slide 19
Results
Thomson parabola spectra
UDMA without gold with gold

## Slide 20
Energy distributions

## Slide 21
D+ ions obtained from deuterated samples

## Slide 22
TPS signals at different pulse durations
12 fs 50 fs 120 fs

## Slide 23
Some CR-39 trace detector results
Trace size distribution in the unshielded area
Target was UDMA-BN
No gold
With gold
1 h etching
3 h etching

## Slide 24
Traces in the shielded region, target: UDMA-D100 deuterated polymer
Exposed to 65 shots, including 12 fs and 120 fs pulses
CR-39 plates evaluation with the help of Julianna Szabó from EK (Energy Research Centre).

## Slide 25
Conclusions
Laser contrast is important, working on improving it in the WRCP laser lab
TPS data analysis is ongoing, results are preliminary
Promising TPS results can be seen with higher energy ions detected with gold nanorods
Also promising CR-39 particle traces seen, but calibration is needed for all kinds of particles and energy ranges
Nuclear detector data still under evaluation, but photon signals were definitely larger for targets with gold nanorods
Sample surface positioning is critical
Future plans for experiments at ELI-ALPS
Find methods to manufacture targets with very good flatness
Find methods to position the sample surface exactly in the focus
Make sure the orientation is also correct and reproducible
Use thin targets (<~ 1 μm)
In the case of thick targets, leave it on the substrate