## Slide 1: The GPU partition of the Komondor supercomputer
Zoltan Juhasz
HPC Competence Centre KIFÜ
University of Pannonia

## Slide 2: HPC Competence Centre – hpc.kifu.hu
Key roles
  HPC user support
  HPC knowledge transfer
  HPC outreach and education, user training
  International cooperation with other EU HPC Competence Centres
Target groups
  academic research community
  government
  industry
  international partners
User and project management
Infrastructure access
User technical support
Technical consulting
Domain Software porting and/or development support
Advanced
Standard
Basic

## Slide 3: The Komondor Supercomputer
HPE CRAY EX System
Compute performance: 6.13 Pflop/s
# 300 on the TOP500 List
4 partitions: CPU, GPU, AI, BigData (EX425 and EX235n Compute Blades, HPE Apollo 6500 Gen10+, HPE Superdome Flex
State-of-the-art technology powering Frontier [#1], Aurora [#2], LUMI [#5], Perlmutter [#12], etc) supercomputers

## Slide 4: The CRAY EX family

## Slide 5: Basic statistics (as of 15 May 2024)
System operational since August 2023
223 active projects, 1000 active users
Number of submitted jobs: 2,672,064
Increasing system utilisation: from 40-50 % (last year) to 80-90 % (current)
partition | # jobs | share
cpu | 1,182,945 | 44.27%
gpu | 1,483,271 | 55.51%
bigdata | 3,193 | 0.12%
ai | 2,655 | 0.10%
ai, gpu (hybrid job) | 2 | 0.00%

## Slide 6: Project statistics – traditional projects
Chart: # trad. projects by scientific field
| ecology | other | mathematics | linguistics | engineering | computer science | biology | chemistry | physics | medicine
 | 0 | 0 | 1 | 5 | 7 | 9 | 9 | 15 | 18 | 27
Chart: # trad. projects by type of computation
| education | other | sequencing | quantum chemistry | other simulations | AI | molecular dynamics
 | 0 | 1 | 6 | 12 | 19 | 28 | 29

## Slide 7: Project statistics – pilot projects
Chart: # pilot projects by scientific field
| other | linguistics | ecology | biology | mathematics | chemistry | engineering | physics | medicine | computer science
 | 3 | 5 | 5 | 6 | 6 | 8 | 10 | 12 | 19 | 30
Chart: # pilot projects by type of computation
| sequencing | quantum chemistry | education | molecular dynamics | other | other simulations | AI
 | 2 | 5 | 8 | 12 | 12 | 27 | 38

## Slide 8: System Architecture
System
Cabinet
Chassis (8 per cabinet)
Blade (8 per chassis)
Node (2 per blade)
1 CPU, 4 GPUs per node

## Slide 9: GPU partition
1 cabinet if fully loaded
  8 x 8 = 64 blades
  64 x 2 x 4 = 512 GPU cards
Komondor GPU part.
  29 blades
  58 nodes
  232 GPUs

## Slide 10: Node architecture (EX235n blade)
Two nodes per blade
Each node has:
  1 AMD EPYC Milan 7763 CPU (64 cores)
  4 Nvidia A100 (Ampere) GPUs
  8 DIMMs per CPU socket (1DPC)
  PCIe 4.0 (32 GB/s) GPU-CPU and NIC-CPU connection
  2 HPE Slingshot 11 NICs (200 Gb/s)
  256 GB of DDR4 DRAM: 204.8 GB/s CPU bw
  40 GB of HBM per GPU with: 1555.2 GB/s GPU bw
  4 third generation NVLink connections between each pair of GPUs, 25 GB/s/direction per link, 200 GB/s total BW point-to-point

## Slide 11: A100 GPU architecture
6912 FP32 CUDA cores (64/SM)
6912 INT32 CUDA cores
3456 FP64 CUDA cores
432 3rd gen Tensor Cores
Peak FP64 | 9.7 TFLOPS
Peak FP64 Tensor Core | 19.5 TFLOPS
Peak FP32 | 19.5 TFLOPS
Peak FP16 | 78 TFLOPS
Peak BF16 | 39 TFLOPS
Peak TF32 Tensor Core | 156 TFLOPS
Peak FP16 Tensor Core | 312 TFLOPS
Performance
SM: Streaming
Multiprocessor
108 SMs in total

## Slide 12: CPU architecture (AMD EPYC Milan 7763 )
Core Complex Die (CCD)

## Slide 13
8 x16 PCI-e I/O ports per CPU

## Slide 14
CPU theoretical peak performance :
39.2 GFlops per core
2.51 TFlops per socket
Instruction-to-bytes ratio:
Roofline performance model

## Slide 15
CPU theoretical peak performance :
39.2 GFlops per core
2.51 TFlops per socket
Instruction-to-bytes ratio:
A100: 12.54 (FP32)
6.24 (FP64)

## Slide 16: Why and when to use multiple GPUs?
Sufficient work
Saturation effect

## Slide 17: GPU partition, chassis internal architecture

## Slide 18: Slingshot 11 interconnect
Ethernet-based switch interconnect, scalable to nearly 300k endpoints
max. 3-hop distance to any node
Dragonfly topology
Rosetta switch (adaptive routing, congestion control, multicast, reduction)
2-3 ms internode point-to-point latency
200 Gb/s bandwidth
Hardware support for MPI operations (one-sided communication, collectives)

## Slide 19: Programming multi-GPUs
Many programming models, configurations and options
1. How to use GPUs?
  Using pre-compiled libraries only
  OpenMP/OpenACC offloading
  CUDA programming
2. How to communicate among nodes and GPUs?
  MPI versions: MPICH vs OpenMPI (host-based or CUDA-Aware)
  NVLink
  NCCL, etc

## Slide 20: Komondor software environment
Module system
CRAY programming environment
MPI versions
GPU specific considerations
CUDA compilation

## Slide 22: Default modules on Komondor
Currently Loaded Modulefiles/prog. environements:
1) craype-x86-rome 5) cce/16.0.1 9) cray-libsci/23.09.1.1
2) libfabric/1.15.2.0 6) craype/2.7.23 10) PrgEnv-cray/8.4.0
3) craype-network-ofi 7) cray-dsmml/0.2.2 11) sbank
4) perftools-base/23.09.0 8) cray-mpich/8.1.27
Other notable modules:
PrgEnv-nvhpc/8.4.0, PrgEnv-nvidia, cudatoolkit/12.3, nvhpc-hpcx-cuda12/23.11, openmpi/5.0.2

## Slide 23: Compiler configuration with modules
Vendor | PrgEnv | Module | Language | Wrapper | Compiler
GNU | PrgEnv-gnu | gcc | C | cc | ${GCC_PATH}/bin/gcc
GNU | PrgEnv-gnu | gcc | C++ | CC | ${GCC_PATH}/bin/g++
GNU | PrgEnv-gnu | gcc | Fortran | ftn | ${GCC_PATH}/bin/gfortran
NVIDIA | PrgEnv-nvidia | nvidia | C | cc | nvc
NVIDIA | PrgEnv-nvidia | nvidia | C++ | CC | nvc++
NVIDIA | PrgEnv-nvidia | nvidia | Fortran | ftn | nvfortran
HPE | PrgEnv-cray | cce | C | cc | craycc
HPE | PrgEnv-cray | cce | C++ | CC | crayCC
HPE | PrgEnv-cray | cce | Fortran | ftn | crayftn

## Slide 24: Example modules

## Slide 25: GPU code compilation
CASE 1: 1-4 GPUs
  cudatoolkit module, nvcc compiler
CASE 2: multinode programs with MPI
  Cray-MPICH: works with separate C/C++ and CUDA source files
  OpenMPI 5.0: can be used with single combined C/CUDA source files

## Slide 26: GPU job execution with SLURM
Use the #SBATCH --gres=gpu:[1-4] option, no jobs will run without this option
Other options
  --gpus-per-task: GPUs required per task. Requires the job to specify a task count.
  --exclusive
  --gpu-bind
  --tasks-per-node
Multi Instance GPU (MIG) is disabled, no hardware partitioning of GPUs

## Slide 27: Scheduling scenarios
Full node: 1 node and 4 GPUs
Multiple full nodes: exactly N x 4 GPUs
Fractions: 1 node, 1 to 3 GPUs
Many GPUs < Nx4 GPUs
Interactive jobs
GPU 0
GPU 1
GPU 2
GPU 3
User 1
User 2
GPU 0
GPU 1
GPU 2
GPU 3
User 1
User 2

## Slide 28: Execution profiling, performance analysis
NSight Systems for program execution information
  includes CUDA kernel, CPU execution info + communication information
NSight Compute for kernel analysis
Command line interface only (nsys, ncu)
Save output report into file, download to local workstation for visualisation

## Slide 29
Example, v.1: 4 OpenMP threads, 4 GPUs, blocking CUDA function calls

## Slide 30
Example v.2: 4 OpenMP threads, 4 GPUs, 4 CUDA streams, async CUDA functions

## Slide 31: GPU partition usage and statistics
Chart: GPU partition utilisation

## Slide 32
1 day
2 days
runtime (hours)
Job runtimes on the GPU partition
submission time
avg queue time:
< 1 hour

## Slide 33
!
Allocated nodes per jobs (1,483,271 jobs) on the GPU partition
Job submission time
Less than 20 projects use more than 2 nodes!
Largest job uses 32 nodes

## Slide 34
allocated nodes

## Slide 35: Summary
The Komondor system is embraced by the research community
Most former supercomputer projects/users migrated
System utilisation is already around 90%
State-of-the-art system, most of the performance in GPU partition
Effective use is not trivial, requires system, hardware and software knowledge/expertise

## Slide 36: Summary
Most current jobs are not true HPC jobs (yet) – very few GPUs per jobs, short execution times
Many programs will require performance analysis, optimisation and tuning
Great opportunity to learn, educate community, build up national HPC expertise
The HPC Competence Centre is here to help
Please send your suggestions, feedback or questions to us at hpc@kifu.gov.hu