## Slide 1: Tensor Core Computing: an example on Independent Component Analysis
University of Pannonia
Veszprem, Hungary
Zeyu Wang, Zoltan Juhasz
May 2024
Notes: Parallel Implementation of Multivariate Empirical Mode Decomposition on GPU

## Slide 2
Content outline
1. Tensor core
1.1 Abstract and hierarchy
1.2 Programming paradigm
2. Independent Component Analysis (ICA)
2.1 Algorithm flow
2.2 Parallel implementation
2.3 Variables analysis
3. Implementation strategy
3.1 Locating matrix multiplication
3.2 Numerical correctness
3.3 Performance preview
4. Future works

## Slide 3
1.1 Abstract and hierarchy of the tensor core
The structure of GA100 SM
D
A
B
C
4x4
4x4
4x4
*
=
=

## Slide 4
Model | Micro-architecture | Launch | CUDA cores | Memory size (GB) | Processing power (TFLOPS) |  | 
 |  |  |  |  | Tensor core FP32 | Single precision | Double precision
V100 | Volta | Jun 21, 2017 | 5120 | 16/32 | 112.2 | 14.0 | 7.0
T4 | Turing | Sept 12, 2018 | 2560 | 16 | 64.8 | 8.1 | 0.2
A100 | Ampere | May 14, 2020 | 6912 | 40/80 | 312.0 | 19.5 | 9.7
H100 | Hopper | Mar 22, 2022 | 14592 | 80 | 756.4 | 51.2 | 25.6
Some GPUs equipped with tensor cores

## Slide 5
1.1 Abstract and hierarchy of the tensor core
Software hierarchy
Hardware hierarchy
D
A
B
C
16x16
*
=
=
warp
Multiple tensor cores
16x16
16x16
Notes: The correspondence is: one warp is handled by multiple tensor cores, or multiple tensor cores are used by one warp, still dynamically/concurrently. And threads within a warp provide a larger 16x16x16 matrix operation to be processed by multiple tensor cores.

## Slide 6
1.2 Tensor core programming paradigm
M
K
K
N
M
N
M
N
*
+
=
A
B
C
D
is a 16*16 submatrix / tile
(1,1)
(1,3)
(1,4)
(3,1)
(1,5)
(1,1)
(3,1)
(4,1)
(5,1)
(1,3)
(1,1)
A(1,1) * B(1,1) + A(1,2) * B(2,1) + A(1,3) * B(3,1) + A(1,4) * B(4,1) + A(1,5) * B(5,1) + C(1,1) = D(1,1)
A(1,1) * B(1,2) + A(1,2) * B(2,2) + A(1,3) * B(3,2) + A(1,4) * B(4,2) + A(1,5) * B(5,2) + C(1,2) = D(1,2)
A(1,1) * B(1,3) + A(1,2) * B(2,3) + A(1,3) * B(3,3) + A(1,4) * B(4,3) + A(1,5) * B(5,3) + C(1,3) = D(1,3)
A(2,1) * B(1,1) + A(2,2) * B(2,1) + A(2,3) * B(3,1) + A(2,4) * B(4,1) + A(2,5) * B(5,1) + C(2,1) = D(2,1)
A(2,1) * B(1,2) + A(2,2) * B(2,2) + A(2,3) * B(3,2) + A(2,4) * B(4,2) + A(2,5) * B(5,2) + C(2,2) = D(2,2)
A(2,1) * B(1,3) + A(2,2) * B(2,3) + A(2,3) * B(3,3) + A(2,4) * B(4,3) + A(2,5) * B(5,3) + C(2,3) = D(2,3)
A(3,1) * B(1,1) + A(3,2) * B(2,1) + A(3,3) * B(3,1) + A(3,4) * B(4,1) + A(3,5) * B(5,1) + C(3,1) = D(3,1)
A(3,1) * B(1,2) + A(3,2) * B(2,2) + A(3,3) * B(3,2) + A(3,4) * B(4,2) + A(3,5) * B(5,2) = C(3,2) = D(3,2)
A(3,1) * B(1,3) + A(3,2) * B(2,3) + A(3,3) * B(3,3) + A(3,4) * B(4,3) + A(3,5) * B(5,3) = C(3,3) = D(3,3)
(2,1)
(1,2)
(1,2)
(1,3)
(1,1)
(1,2)
(1,3)
column major
column major
column major
column major
is a warp
thread grid
2D thread grid
Loop over K (accumulated by each warp)
wmma::fragment< >
wmma::load_matrix_sync< >
wmma::mma_sync< >
wmma::store_matrix_sync< >
Notes: 1.2 Tensor core programming paradigm (with code demo together)
One warp is responsible to a set of 16*16*16 operation, also, one warp is in charge of one tile in the result matrix.
When designing the kernel function, we need to make sure all the threads in the same warp know which tile in A and B they should point to.
So, what is exposed to the users or what we need to be concerned about is the mapping between different warps and different 16*16 tiles in the D=A*B+C process. As for “which fragment in the tile is scheduled to which thread and handled by which tensor core” is opaque to us.
wmma::fragment
Codes shouldn’t be shown, just put the key lines in the kernel function code.

## Slide 7
2.1 Independent Component Analysis (ICA)
Measured EEG signals
True brain signal
Unknown
Mixing

## Slide 8
2.1 Algorithm flow
Unmixing matrix
Independence criterion
…
…
…
Whitened data
…
Update
The process of solving the unmixing matrix
Raw data
Centralized data
Whitened data
Singular Value Decomposition
Notes: More equations about the matrix rotation and starching, SVD

## Slide 9
1. Initialize
2. while (not converged and < limit)
2.1 Y = permutate(X)
2.2 for each block B in signal Y
2.2.1
2.2.2
2.2.3
2.2.4 update bias
end for
end while
CUDA ICA
2.2 Parallel implementation
Notes: There are a lot of matrix matrix multiplication operations in each iteration.

## Slide 10
2.3 Variables analysis
u (ch*b)
y (ch*b)
yu (ch*ch)
weights (ch*ch)
data (ch*s)
Step1
Step2
Step3
Step4
pdf
permute (s*1)
bias (ch*1)
bsum (ch*1)
u (ch*b)
y (ch*b)
sign (ch*1)
bsum (ch*1)
y (ch*b)
weights (ch*ch)
data (ch*s)
bias (ch*1)
yu (ch*ch)
y (ch*b)
u (ch*b)
weights (ch*ch)
bias (ch*1)
sign (ch*1)
yu (ch*ch)
bsum (ch*1)
sign (ch*1)
numChannels = ch : not modified
numSamples = s : modified
blockLength = b

## Slide 11
3.1 Locating matrix multiplication
u = weights * data
y = -tanh(u/2)
use bias?
u = u + bias
yes
no
y
u
weights
data
bias
Step 1
bsum = sum(y)
Step 2
y
bsum
yu = y * u’
yu = yu + I
Step 3
yu
y
u
weights = lrate * yu * weights + weights
use bias?
bias = lrate * bsum + bias
bias
yes
weights
no
Step 4
bsum
yu
: FMA operation
1. Initialize
2. while (not converged and < limit)
2.1 Y = permutate(X)
2.2 for each block B in signal Y
2.2.1
2.2.2
2.2.3
2.2.4 update bias
end for
end while

## Slide 12
3.2 Numerical correctness
The diagonal lines produced by IC pairs from
MATLAB-ICA and CUDAICA
The diagonal lines produced by IC pairs from
tensor core ICA and CUDAICA
Notes: There are 4 cased

## Slide 13
3.3 Performance preview
32-channel EEG data, up to 210k time points, CUDA core and tensor core execution time are produced by A100 GPU on Komondor supercomputer. The MATLAB execution time is produce by a 8-core CPU (i7-9700k)
4x speedup
3x speedup
Notes: Regardless of correctness, ideal performance
Matlab version

## Slide 14
4 Future works
Numerical correctness issue
Tensor core + shared memory strategy
Further performance testing
  New strategy and larger dataset
  EEG processing pipeline integration
Impact of mixed precision computing
  FP32, TF32, FP16, BF16 ……
Other potential algorithms that tensor cores can optimize
  Are there a lot of matrix multiplication operations in the algorithm? Why not consider using tensor cores to speed it up?

## Slide 15
This research is supported by
Új Nemzeti Kiválóság Program (UNKP)

## Slide 16
Decorrelation
Samples
Channels
Diagonalization
Data matrix
Covariance
Covariance matrix
Diagonal matrix
Notes: One of the measure of the correlation between two variables is the covariance, and we use the covariance matrix to measure the correlation between the channels of the EEG data, what we want finally is this kind of diagonal form covariance matrix, that means there is no correlation between each channel.
Decorrelation
Our first task is to decorrelated the channels,
Centralize the data matrix, multiple the eigenvector matrix of 〖(𝑋·𝑋〗^𝑇)

## Slide 17
Raw data
Centralized data
Whitened data
Decorrelation
Raw data
Centralization
Whitened data
Decorrelated data
Centralized data
Covariance
matrix
Eigenvalue decomposition
Eigenvector matrix
Eigenvalue matrix
^(-0.5)
Notes: The specific approach is the centralization and whitening, first we subtract the mean of the raw data and calculate its covariance matrix, next we get the eigenvector matrix to multiply the centralized data matrix to achieve the decorrelation.
From the graphic perspective, what we are doing is the rotation and stretching of the raw signal matrix.
The decorrelation process is also called sphering processing, because the distribution of the data is changed to a sphere.
Centralize the data matrix, multiple the eigenvector matrix of 〖(𝑋·𝑋〗^𝑇)
The decorrelation process is also called sphering processing, because the distribution of the data is changed to a sphere.
For Gaussian distributed data, decorrelation is equivalent to independence.

## Slide 18
Set

## Slide 19
Remove dependency
Unmixing matrix
Independence criterion
…
…
…
Whitened data
…
Update
The process of solving the unmixing matrix
Notes: The next step is to remove the dependency,
The whitened data will be computed by the unmixing matrix and the non-linear function, and then we will assess the independence of the output signals, if it doesn’t meet the requirements, we will implement a back propagation to update the unmixing matrix, after some iterations, the independence of the output signals will be improved, and we will achieve our purpose of separating the signals.
So the key here is to figure out how to measure dependency, how to determine the loss function.