## Slide 1: Recent developments in open-source design tools and QPUs
www.meetiqm.com
E. Takala1, T. Mylläri1, J. Räbinä1, P. Smirnov1
M. Malinen2, P. Råback2, J. Ruokolainen2, J. Kataja2
WE BUILD QUANTUM COMPUTERS
1 IQM Quantum Computers ltd, Finland
2 CSC – It Center for Science ltd, Finland

## Slide 2: KQCircuits by IQM – global leader in building quantum computers
https://github.com/iqm-finland/KQCircuits

## Slide 3
Simulations
Ansys
  Q3D – capacitance extraction using method of moments
  HFSS – S matrix extraction
  HFSS Eigenmode with ideal inductors modelling junctions/SQUIDs
  pyEPR support [1]
Elmer (Open-source FEM solver by CSC Finland) [2]
  2D cross-section and 3D Simulations (capacitance, inductance, s-matrix)
    Waveguide media properties for arbitrary cross-sections (impedance and capacitance)
    Kinetic inductance for some penetration depth
    Energy participation ratio (EPR)
FEM component in KQC workflow quite replaceable with other third-party simulator software as we learn about them (e.g. Sonnet, AWS Palace https://awslabs.github.io/palace/stable/)
[1] Z. K. Minev et al., ‘Energy-participation quantization of Josephson circuits’, npj Quantum Inf, vol. 7, no. 1, Art. no. 1, Aug. 2021
[2] P. Råback et al., ‘Elmer’. CSC – IT Center for Science, Available: github.com/ElmerCSC/elmerfem
https://www.ansys.com/
https://www.csc.fi/fi/web/elmer
https://www.sonnetsoftware.com/

## Slide 4: There is MUCH more – go and see KQCircuits presentation at FSIC2023!
For more information about KQCircuits capabilities available online, detailed presentation by P. Smirnov (video available):
https://wiki.f-si.org/index.php?title=KQCircuits_%E2%80%93_open-source_EDA_software_for_designing_chips_with_super_conducting_qubits

## Slide 5: Case study: Hanger resonator
lambda/2 resonator s-parameters
computed using a network model
Also with KQC-Elmer (peak ﬁnding algorithm)
Nedelec linear and quadratic elements underestimate resonance and 2nd kind overestimates it
Penetration depth (100 nm) decreases resonance frequency
Metal thickness (200 nm) increases resonance frequency
https://github.com/iqm-finland/KQCircuits/blob/main/klayout_package/python/scripts/simulations/hanger_resonator_sim.py

## Slide 6: Elmer full wave simulation - chip example

## Slide 7: Case study: EPR with MER – Double pads
Metal Edge Regions (MER)
  Automatically generated
  Divided into regions (user specified)
  Each region can be associated with a 2D cross-section
2D cross-section
  Automatically generated
  User gives coordinates on chip (two points define a cross-section location)
In the example we have four regions:
  1cplr, 2cplr, wire and default
Four loss groups: ma, sa, ms, substrate
Default is the region that is not explicitly defined
MERs

## Slide 8: Corrected EPR
Only total energy is computed in 3D metal edge regions
2D simulation models implement interfaces in detail
3D total energy is corrected using 2D cross-section simulation
Interfaces are modeled in 2D
Only total energy computed in MERs
MER box in 2D corresponds to that in 3D
wire
2cplr
1cplr
Vacuum
Substrate
MA
SA
MS

## Slide 9: EPR – participation and loss
Energy participation and loss can be grouped by a cross product of region (wire, 1cplr, 2cplr, default), loss group (MA, SA, MS, Substrate, Vacuum) and MER/non-MER
wire
2cplr
1cplr
Default contains everything else

## Slide 10: Crystals and Stars
Qubit Crystal
Qubits and tunable couplers
Fast parallel gates
Resonator Star
Qubits, tunable couplers and computational resonators
One-to-all connectivity

## Slide 11: Qubit Crystals
IQM-5
5 qubits
4 couplers
Air-bridges or flip-chip
Produced at scale
IQM Garnet
20 qubits
30 couplers
Flip-chip
Produced at scale
IQM-54
54 qubits
70 couplers
Through Silicon Via
Acceptance testing
IQM-150
150 qubits
266 couplers
Through Silicon Via
First cooldown during 2024
W48.2

## Slide 12: Qubit lifetime [1]
QPU qubits
Test device qubits
[1] Heinsoo et al., am. phys. soc. W48.2 (2024)

## Slide 13: Benchmarks [1]
IQM Garnet™ A
20
Qubit count
32
Quantum volume
(Classical simulation complexity)
11
Q-score
(Max-cut task size)
20
Largest GHZ genuinely entangled state
CLOPS
2600
(Computation rate)
median 99.91 %
1Q fidelity
best 99.944 ± 0.003 %
median 99.51 %
2Q fidelity
best 99.8 ± 0.5 %
Single qubit gate
Two qubit gate
QPU
Test device

## Slide 14: Conclusions
IQM QPUs designed using KQCircuits
Fully open-source simulator available
Semi-automatic EPR MER method available
Median single-qubit gate error below
Median two-qubit gate error below
Competitive 20 qubit machine produced at scale
More than 50 contributors from IQM
Collaboration with VTT
Acknowledgements
eelis@meetiqm.com

## Slide 15: Appendix

## Slide 16: QPU design process
Hamiltonian
Circuit
Geometry
KQC
Mask Layout
KQC
Fabrication
Validation
Netlist, DRC, Full FEM
(enabled by KQC)
Element library
Components FEM
(enabled by KQC)

## Slide 17: Interface loss references
[28] W. Woods et al., ‘Determining Interface Dielectric Losses in Superconducting Coplanar-Waveguide Resonators’, Phys. Rev. Applied, vol. 12, no. 1, p. 014012, Jul. 2019. [30] M. V. P. Altoé et al., ‘Localization and Mitigation of Loss in Niobium Superconducting Circuits’, PRX Quantum, vol. 3, no. 2, p. 020312, Apr. 2022. [95] C. Wang et al., ‘Surface participation and dielectric loss in superconducting qubits’, Appl. Phys. Lett., vol. 107, no. 16, p. 162601, Oct. 2015. [143] M. P. F. Graça et al., ‘Electrical analysis of niobium oxide thin films’, Thin Solid Films, vol. 585, pp. 95–99, Jun. 2015. [144] J. Verjauw et al., ‘Investigation of Microwave Loss Induced by Oxide Regrowth in High-Q Niobium Resonators’, Phys. Rev. Applied, vol. 16, no. 1, p. 014018, Jul. 2021. [145] J. Krupka et al., ‘Measurements of Permittivity and Dielectric Loss Tangent of High Resistivity Float Zone Silicon at Microwave Frequencies’, in 2006 International Conference on Microwaves, Radar & Wireless Communications, Krakow, Poland, May 2006, pp. 1097–1100.