## Slide 1: Laser-Ion Acceleration using Gold Nanorods
Dr. Chris Grayson
For plasmonic enhancement of Fusion reactions
The NanoPlasmonic Laser Induced Fusion Energy (NAPLIFE)

## Slide 2: Laser Fusion
Our goal is to use low energy lasers to accelerate ions to produce nonequilbirum nano fusion.
Equilibrium fusion requires enormous energies and densities
NIF – 2 MJ
plasmonics
20 mJ
~100 nm
HAC inaugrial lecture RafelskiCite lecture
10^-8

## Slide 3: Laser Fusion
Our goal is to use low energy lasers to accelerate ions to produce nonequilbirum nano fusion.
Aneutronic proton-boron fusion
p+11B → (3 4He) + 8.7 MeV
*Equilibrium fusion requires enormous energies and densities*
NIF – 2 million joules
plasmonics

## Slide 4: Laser Fusion
Our goal is to use low energy lasers to accelerate ions to produce nonequilbirum nano fusion.
Aneutronic proton-boron fusion
p+11B → (3 4He) + 8.7 MeV
Corresponds to ~0.1 picojoule per particle
*Equilibrium fusion requires enormous energies and densities*
NIF – 2 million joules

## Slide 5: Laser Fusion
Our goal is to use low energy lasers to accelerate ions to produce nonequilbirum nano fusion.
Aneutronic proton-boron fusion
p+11B → (3 4He) + 8.7 MeV
Corresponds to ~0.1 picojoule per particle
Typical laser pointers have times more energy
(5 mJ)
*Equilibrium fusion requires enormous energies and densities*
NIF – 2 million joules

## Slide 6: Laser Fusion
Our goal is to use low energy lasers to accelerate ions to produce nonequilbirum nano fusion.
Aneutronic proton-boron fusion
p+11B → (3 4He) + 8.7 MeV
Corresponds to ~0.1 picojoule per particle
Typical laser pointers have times more energy but the energy is not sufficiently focused.
(5 mJ)
*Equilibrium fusion requires enormous energies and densities*
NIF – 2 million joules

## Slide 7: Laser Fusion
Our goal is to use low energy lasers to produce nonequilbirum fusion reactions .
Typical laser pointers have times more energy but the energy is not sufficiently focused.
(5 mJ)
Notes: 1 MeV is the cutoff energy of TNSA electrons

## Slide 8: Laser Fusion
Our goal is to use low energy lasers to produce nonequilbirum fusion reactions .
Focus in time
Pulsed laser
Temporal compression
High peak power
5mW
50 GW
( W)
Femtosecond scale pulses
Allows for nanoscale particle acceleration
Typical laser pointers have times more energy but the energy is not sufficiently focused.
(5 mJ)
Notes: 1 MeV is the cutoff energy of TNSA electrons

## Slide 9: Laser Fusion
Our goal is to use low energy lasers to produce nonequilbirum fusion reactions .
Focus in time
Pulsed laser
Temporal compression
High peak power
5mW
50 GW
( W)
Femtosecond scale pulses
Allows for nanoscale particle acceleration
Typical laser pointers have times more energy but the energy is not sufficiently focused.
(5 mJ)
Light cannot be focused past the diffraction limit
400 nm
MeV/nm3
Notes: 1 MeV is the cutoff energy of TNSA electrons

## Slide 10: Laser Fusion
Our goal is to use low energy lasers to produce nonequilbirum fusion reactions .
Focus in time
Pulsed laser
Temporal compression
High peak power
5mW
50 GW
( W)
Femtosecond scale pulses
Focus in space
Couple to massive electron wave
Surface Plasmon Resonance (LSPR)
Allows for nanoscale particle acceleration
Typical laser pointers have times more energy but the energy is not sufficiently focused.
(5 mJ)
Light cannot be focused past the diffraction limit
400 nm
MeV/nm3
Focuses light past the diffraction limit
Our Novel Approach
Notes: 1 MeV is the cutoff energy of TNSA electrons

## Slide 11
The NanoPlasmonic Laser Induced Fusion Energy
How can nano-structured targets lead to femtosecond scale ion acceleration?
Huge Energy mismatch between laser and Fusion threshold
“Atomic”
“Nuclear”
50,000 photons

## Slide 12
The NanoPlasmonic Laser Induced Fusion Energy
Locally increased Electric field Strength and Field Gradient
Solution
Use collective electron motion.
like (TNSA)
(Nuclear Scale)
Huge Energy mismatch between laser and Fusion threshold
How can nano-structured targets lead to femtosecond scale ion acceleration?

## Slide 13
The NanoPlasmonic Laser Induced Fusion Energy
These nanorods resonantly absorb light via Localized Surface Plasmon resonance (LSP)
The classical polarizability diverges when
Maier, Stefan A. Plasmonics: fundamentals and applications. Vol. 1. New York: springer, 2007.
LSP resonance can respond incredibly fast.
Locally increased Electric field Strength and Field Gradient
(Nuclear Scale)
Huge Energy mismatch between laser and Fusion threshold
Solution
Use collective electron motion.
like (TNSA)
Antennas For Light
How can nano-structured targets lead to femtosecond scale ion acceleration?

## Slide 14
The NanoPlasmonic Laser Induced Fusion Energy
These nanorods resonantly absorb light via Localized Surface Plasmon resonance (LSP)
Huge Energy mismatch between laser and Fusion threshold
Solution
Use collective electron motion.
like (TNSA)
Antennas For Light
(Fusion threshold)
Bonyár, A. et al. Int. J. Mol. Sci. 2022, 23, 13575.
Locally increased Electric field Strength and Field Gradient
How can nano-structured targets lead to femtosecond scale ion acceleration?

## Slide 15
The NanoPlasmonic Laser Induced Fusion Energy
These nanorods resonantly absorb light via Localized Surface Plasmon resonance (LSP)
Huge Energy mismatch between laser and Fusion threshold
Solution
Use collective electron motion.
like (TNSA)
Antennas For Light
(Fusion threshold)
Locally increased Electric field Strength and Field Gradient
Near Field Enhancement (NFE) of the electric field around the Nano rods causes increased ion acceleration
The electric field around the nanorod is enhanced over the background laser field on the scale of 10’s of nm
Field enhancement and absorption measured at low intensity: W/cm2
M. Csete Group: Dávid Vass, Emese Tóth, András Szenes, Balázs Bánhelyi
How can nano-structured targets lead to femtosecond scale ion acceleration?

## Slide 16
The NanoPlasmonic Laser Induced Fusion Energy (NAPLIFE)
UDMA-TEGMA (polymer)
(not to scale)
The NAPLIFE project introduces nanostructured laser targets to generate more efficient proton acceleration for ultra-fast pulsed lasers.
Tamas
Biro
Norbert
Kroo
Joined Sept. 2024
Many other initiatives use nanostructures to enhance ion acceleration – ours is unique in that we use resonant localized plasmons (LSPR).
And many more!
Márk Aladi
Miklós Kedves

## Slide 17
The NanoPlasmonic Laser Induced Fusion Energy (NAPLIFE)
UDMA-TEGMA (polymer)
(not to scale)
The NAPLIFE project introduces nanostructured laser targets to generate more efficient proton acceleration for ultra-fast pulsed lasers.
Tamas
Biro
Norbert
Kroo
Joined Sept. 2024
Many other initiatives use nanostructures to enhance ion acceleration – ours is unique in that we use resonant localized plasmons (LSPR).
And many more!
Márk Aladi
Miklós Kedves

## Slide 18
The NanoPlasmonic Laser Induced Fusion Energy (NAPLIFE)
UDMA-TEGMA (polymer)
(not to scale)
The NAPLIFE project introduces nanostructured laser targets to generate more efficient proton acceleration for ultra-fast pulsed lasers.
Tamas
Biro
Norbert
Kroo
Joined Sept. 2024
Many other initiatives use nanostructures to enhance ion acceleration – ours is unique in that we use resonant localized plasmons (LSPR).
UDMA-TEGMA (polymer)

## Slide 19
The NanoPlasmonic Laser Induced Fusion Energy
Nanorod doped samples led to exponential energy deposition in the target.
- Nanorods
- Control
Wigner Experimental Results
EPOCH 3D PIC Simulation of Surface plasma
Higher maximum proton energy
Nanorods lead to increased proton acceleration in EPOCH Simulations
NAPLIFE Previous Results
István Papp et al. 2023 arXiv:2306.13445v2
Ágnes Szokol et al. arXiv:2402.18138

## Slide 20
The NanoPlasmonic Laser Induced Fusion Energy
Nanorod doped samples led to exponential energy deposition in the target.
- Nanorods
- Control
EPOCH 3D PIC Simulation of Surface plasma
Higher maximum proton energy
Nanorods lead to increased proton acceleration in EPOCH Simulations
NAPLIFE Previous Results
What causes direct proton acceleration?
- Use this knowledge to tune nanostructures for better acceleration
Wigner Experimental Results
István Papp et al. 2023 arXiv:2306.13445v2
Ágnes Szokol et al. arXiv:2402.18138

## Slide 21: Proton Acceleration from Nanoplasmons
The acceleration of protons and ions in the pre-plasma, is simulated with the EPOCH (Particle in Cell) simulation software in 3D for a single nanorod.
The output of PIC programs can tell you with accuracy what proton energies you will get but not the mechanisms by which they are accelerated
Laser is approximately a plane wave on the scale of the nanorod
Laser light (795 nm, I~W/) impinges on Gold nanorod (~85 nm)
Using PIC to determine this dependencies requires a huge amount of computation time and data storage.

## Slide 22: Proton Acceleration from Nanoplasmons
Simple theoretical calculations motivated by simulation can serve as efficient guiding principles to determine how to perform experiments and simulations.
Laser is approximately a plane wave on the scale of the nanorod
Laser light (795 nm, I~W/) impinges on Gold nanorod (~85 nm)
+
We will focus on forces that come directly from the nanorod the ponderomotive force and Coulomb Explosion
Goal: make simplest model possible and compare to experiment

## Slide 23: Plasmonic Ponderomotive Force
the term is ~1600 times larger for the nanorod than the laser by field enhancement.
keV nm
Typically, the ponderomotive force is far too small to cause direct acceleration to protons due to their large mass.
However, the ponderomotive force due to the oscillating field around a nanorod can be much larger due to field enhancement and increase in the field gradient.
Increase in the ponderomotive force leads to more efficient electron and ion acceleration
Drift force due to the oscillating electron cloud around the gold nanorod due to LSP resonance that could directly couple to ions.
proton
electron
3D Simulations of Single Nanorods
Using EPOCH
Near field approx.

## Slide 24
Proton
(Ionized H)
(for demonstration purposes)
Conducting shell
nm
Toy Model – Conducting Sphere
Dipole moment decide the field strength outside the nanorod
V/m
proton

## Slide 25
If the laser frequency is much larger than the characteristic timescale of proton acceleration
Proton
(Ionized H)
Toy Model – Conducting Sphere

## Slide 26: Simulations on GPU Cluster
y
x
z
4 nm
The 3D nanorod simulation study's the plasmonic effects of a single nanorod (made partially by me and the previous postdoc István Papp)
Simple model contains a gold cylinder with spherical end caps (85x25 nm) at solid density with charge state covered with a neutralizing cloud of “conducting” electrons. The nanorod is surrounded by an ionized medium of carbon and hydrogen. The nanorod is then illuminated with light with some pulse duration with open boundary conditions for fields and particles run for 200 fs.
Focus on analyzing evolution of:
Electric field
Charge density
Number density
Particle energies
Ion Energy spectra – observable via Thompson parabola in experiment.

## Slide 27: Ion spectra -EPOCH
Cutoff energies scale with Z
Plotted in python
Taken at

## Slide 28: Proton Acceleration
What causes late time momentum increase?
Laser pulse duration
y
x
z

## Slide 29: Electron Density
Ionization
After this point the nanorod is heavily ionized
Ionization limit was set to , but ionization can go up to
y
x
z
Electron loss is exaggerated here due to small simulation size

## Slide 30: Electron Density
Ionization
After this point the nanorod is heavily ionized
Ionization limit was set to , but ionization can go up to
Electron loss is exaggerated here due to small simulation size
+
y
x
z
+
+
+
+
+
+
+
+
+
+
Highly ionized gold nanorod causes a Coulomb explosion in the local material.

## Slide 31: Electron Density
Ionization
After this point the nanorod is heavily ionized
Ionization limit was set to , but ionization can go up to
Electron loss is exaggerated here due to small simulation size
+
y
x
z
+
+
+
+
+
+
+
+
+
+
Highly ionized gold nanorod causes a Coulomb explosion in the local material.
How important is coulomb explosion for ion spectra?

## Slide 32: Ion spectra –Coulomb Explosion
+
y
x
z
+
+
+
+
+
+
+
+
+
+
No
Laser

## Slide 33: Ion spectra - Comparison
Coulomb Exp
Ponderomotive + Coulomb Exp
Cutoff energies mainly due to Coulomb Explosion

## Slide 34: Ion spectra - Comparison
Coulomb Exp
Ponderomotive + Coulomb Exp
Cutoff energies mainly due to Coulomb Explosion
Why is the ponderomotive force so small?

## Slide 35: Why is the Ponderomotive effect on ions so small?
similar results found in a previous publication
I. Papp (2022)
EPOCH predicts very small near field enhancement (NFE) in comparison to theory.

## Slide 36: Simulations
y
x
z
5 nm
The 3D nanorod simulation study's the plasmonic effects of a single nanorod
gold cylinder with spherical end caps (85x25 nm) at solid density with charge state covered with a neutralizing cloud of “conducting” electrons. The nanorod is surrounded by an ionized medium of hydrogen. The nanorod is then illuminated with light with some pulse duration with open boundary conditions for fields and particles run for 200 fs.
Measure the Near Field Enhancement Predicted by Epoch
Calculate Average

## Slide 37
At 1 nm from
The surface
55 simulations
2,200 fs
11hrs – Wall hours
704 – CPU hours

## Slide 38
At 1 nm from
The surface

## Slide 39
At 1 nm from
The surface
UDMA
Vacuum

## Slide 40
At 1 nm from
The surface
UDMA

## Slide 41
At 1 nm from
The surface
UDMA
Plasmonic field saturates at the field strength of a fully ionized nanorod
The near field enhancement cannot go above the ionization field of the nanorod
+
y
x
z
+
+
+
+
+
+
+
+
+
+

## Slide 42
At 1 nm from
The surface
UDMA
Plasmonic field saturates at the field strength of a fully ionized nanorod
The near field enhancement cannot go above the ionization field of the nanorod
+
y
x
z
+
+
+
+
+
+
+
+
+
+
The nanorod cannot support a coherent oscillating electric field above this limit.

## Slide 43: Conclusion
For low density of nanorods unoriented, short pulse duration and high intensity (). The dominant acceleration process is coulomb explosion.
In the future we will use nanorod arrays which can reduce electron spillage by sharing electrons.
  Preliminary results show that arrays lead to larger peak energies for ions and increase in electron temperature .
  Previously shown for non-resonant nanorods Vallières et al. (2021)
For ponderomotive nanorod acceleration one must use low intensity and long pulse duration, and structured nano targets, such that protons will continue to acquire energy from multiple nano rods.
Next week we go to ELI in Szeged for more measurements!
Notes: Ad near field enhancement add slide describing simulation

## Slide 44
The NanoPlasmonic Laser Induced Fusion Energy
These nanorods resonantly absorb light via Localized Surface Plasmon resonance (LSP)
The classical polarizability diverges when
This leads to quantum effects such as focusing past the diffraction limit, resonant absorption of light, and electric field enhancement.
Maier, Stefan A. Plasmonics: fundamentals and applications. Vol. 1. New York: springer, 2007.
LSP resonance can respond incredibly fast.
Locally increased field Strength and Field Gradient
Resonance condition

## Slide 45: Why is the NFE effect on ions so small?
similar results found in a previous publication
I. Papp (2022)
EPOCH predicts very small near field enhancement (NFE) in comparison to theory at high intensities.

## Slide 46: Simulations
y
x
z
5 nm
The 3D nanorod simulation study's the plasmonic effects of a single nanorod
gold cylinder with spherical end caps (85x25 nm) at solid density with charge state covered with a neutralizing cloud of “conducting” electrons. The nanorod is surrounded by an ionized medium of hydrogen. The nanorod is then illuminated with light with some pulse duration with open boundary conditions for fields and particles run for 200 fs.
Measure the Near Field Enhancement Predicted by Epoch
Calculate Average

## Slide 47
At 1 nm from
The surface
55 simulations
2,200 fs
11hrs – Wall hours
704 – CPU hours
-fairly cheap simulation

## Slide 48
At 1 nm from
The surface

## Slide 49
At 1 nm from
The surface
UDMA
Vacuum

## Slide 50
At 1 nm from
The surface
UDMA

## Slide 51: Conclusion
Open Questions and Improvements:
Tailor medium to better represent UDMA
Why does the resonance decrease at high intensity?
NFE does not decrease due to ionization….
  Why is there a late time NFE?
  Can the phenomena responsible for this be used to create more resonance at higher intensities?
Measure the Near Field Enhancement Predicted by Epoch
Ionization of electrons

## Slide 52: Thompson parabola spectra

## Slide 53: Thompson parabola spectra

## Slide 54: Thompson parabola spectra

## Slide 55: Thompson parabola spectra

## Slide 56: Thompson parabola spectra

## Slide 57: Thompson parabola spectra
Run statistics over all the days of shots

## Slide 58: Thompson parabola spectra
Chart: 90th Percentile Energy
| UDMA-AU2_RE | BN_M-AU2_RE | UDMA-AU0 | D100-AU2_NR | D100-AU2_RE | D100-AU0 | BN_M-AU0 | UDMA-AU2_NR | D100-AU2_RE(USED) | UDMA-AU3_RE
 | 88.3021 | 87.0769 | 86.0846 | 85.1786 | 83.8371 | 80.2259 | 77.7093 | 69.613 | 69.0391 | 55.8403

## Slide 59
The NanoPlasmonic Laser Induced Fusion Energy
These nanorods resonantly absorb light via Localized Surface Plasmon resonance (LSP)
The classical polarizability diverges when
This leads to quantum effects such as focusing past the diffraction limit, resonant absorption of light, and electric field enhancement.
Maier, Stefan A. Plasmonics: fundamentals and applications. Vol. 1. New York: springer, 2007.
LSP resonance can respond incredibly fast.
Locally increased field Strength and Field Gradient
Can nano-structured targets lead to femtosecond scale ion acceleration?
Huge factor to overcome
Solution
Use collective electron motion.
like (TNSA)

## Slide 60: Plasmonic Ponderomotive Force
proton
the term is ~1600 times larger for the nanorod than the laser by field enhancement.
keV nm
electron
Typically, the ponderomotive force is far too small to cause direct acceleration to protons due to their large mass.
However, the ponderomotive force due to the oscillating field around a nanorod can be much larger due to field enhancement and increase in the field gradient.
Our group was mainly interested in forces due to the oscillating electron cloud around the gold nanorod due to LSP resonance that could directly couple to ions.
(for a proton)

## Slide 61: Ion spectra -EPOCH
Taken at
Periodic Boundary conditions for particles

## Slide 62: Ion spectra -EPOCH
Cutoff energies scale with Z - Coulomb
Peak Energies scale with -Ponderomotive
Taken at
Periodic Boundary conditions for particles

## Slide 63: Ion spectra -EPOCH
Cutoff energies scale with Z - Coulomb
Peak Energies scale with -Ponderomotive
Taken at
Periodic Boundary conditions for particles

## Slide 64: Ion spectra -EPOCH
Cutoff energies scale with Z - Coulomb
Peak Energies scale with -Ponderomotive
Taken at
Periodic Boundary conditions for particles

## Slide 65: Ion spectra -EPOCH
Ponderomotive potential is saturated
Taken at
Periodic Boundary conditions for particles

## Slide 66: Ion spectra -EPOCH
Taken at
Single nanorod

## Slide 67: Ion spectra -EPOCH
Taken at
Nanorod array

## Slide 68: Ion spectra -EPOCH
Taken at
Plasmonic