## Slide 1: Quantum computing platforms and related experimental activities
Ádám Gali
Academia-Industry Matching Event (AIME25)
November 27-28, 2025, 15:30-16:00, HUN-REN Headquarters, Budapest (Hungary)
HUN-REN Wigner Research Centre for Physics
Budapest University of Technology and Economics

## Slide 2
Quantum information processing
Scalable and controllable quantum bits (qubits): long coherence time
Universal quantum gates
Production of “flying” qubits are needed for quantum information processing
  single photon emitters
Di Vincenzo’s five + two criteria
Scalable quantum memory
Ability to initialize qubits
Universal quantum gates
Qubit readout
Long coherence times for qubits
Interconversion between stationary and flying qubits
Faithful transmission of flying qubits
Richard. P. Feynman
Pioneer quantum computer scientists:
Peter Shor Lov Grover

## Slide 3
Photonics quantum simulation and computation
The key bottleneck is photon loss, compounded by the lack of nearly perfect deterministic photon sources and low-loss components
@Wigner RCP: development of multiplexed single photon sources that may drive the optical quantum chip @ELTE
Jian-Wei Pan et al., Nature Photonics volume 19, pages 387–391 (2025)

## Slide 4
Potential quantum bit materials
Materials system | ¦0⟩ | ¦1⟩
Ion traps/Neutral atoms |  | 
Point defects in solids |  | 
Semiconductor quantum dots |  | 
Superconductor circuits |  | 
Topological quantum bits |  | 
Topological quantum bits (e.g., Majorana fermions) would guarantee fault-tolerant quantum computers.
James N. Eckstein and Jeremy Levy, MRS Bulletin 38, 783, (October 2013)

## Slide 5
Towards topological quantum bits
10 mK temperatures
Experimental topological quantum bit research @BME
Theoretical research (on materials) @Wigner RCP and @BME

## Slide 6
Potential quantum bit materials
Materials system | ¦0⟩ | ¦1⟩
Ion traps/Neutral atoms |  | 
Point defects in solids |  | 
Semiconductor quantum dots |  | 
Superconductor circuits |  | 
Topological quantum bits |  | 
Superconductor circuits readout by microwave resonator and/or fields.
James N. Eckstein and Jeremy Levy, MRS Bulletin 38, 783, (October 2013)

## Slide 7
Superconductor circuits quantum computer
10-20 mK temperatures
No experimental research group in Hungary is working on it; low-temperature physics expertise is available @BME and @Wigner RCP
Benchmarking of these quantum computers @Wigner RCP and @ELTE

## Slide 8
Potential quantum bit materials
Materials system | ¦0⟩ | ¦1⟩
Ion traps/Neutral atoms |  | 
Point defects in solids |  | 
Semiconductor quantum dots |  | 
Superconductor circuits |  | 
Topological quantum bits |  | 
Semiconductor quantum dots qubits are read out by spin-selective quantum tunelling.
James N. Eckstein and Jeremy Levy, MRS Bulletin 38, 783, (October 2013)

## Slide 9
Semiconductor quantum dots
cryogenic temperatures
No experimental research group in Hungary is working on it; theory @BME

## Slide 10
Potential quantum bit materials
Materials system | ¦0⟩ | ¦1⟩
Ion traps/Neutral atoms |  | 
Point defects in solids |  | 
Semiconductor quantum dots |  | 
Superconductor circuits |  | 
Topological quantum bits |  | 
Quantum optics for readout and initialization with electron and nuclear spins acting as qubits
James N. Eckstein and Jeremy Levy, MRS Bulletin 38, 783, (October 2013)

## Slide 11
Ion traps and neutral atoms
Neutral atoms quantum computer
Ultrahigh vacuum and cryogenic temperatures
Scalability is an issue
Ultrahigh vacuum
>10,000 physical qubits
@Wigner RCP: technology of ultrahigh vacuum for neutral atoms

## Slide 12
Potential quantum bit materials
Materials system | ¦0⟩ | ¦1⟩
Ion traps/Neutral atoms |  | 
Point defects in solids |  | 
Semiconductor quantum dots |  | 
Superconductor circuits |  | 
Topological quantum bits |  | 
Readout of solid state defect spins:
Spin-dependent transport (current)
Spin-dependent optical signal (luminescence)
Physics of solid state point defect qubits:
Precise placement of defects in a clean host environment
Ultra-precise magneto-optical measurements & spectral analysis
James N. Eckstein and Jeremy Levy, MRS Bulletin 38, 783, (October 2013)

## Slide 13
Some Important Spectroscopic Methods for Defects
Physics of Point Defects
Photoluminescence
Electron spin resonance (ESR/EPR), electron–nuclear double resonance (ENDOR)
Photo-electron spin resonance: optical spin polarisation, leading to an enhanced ESR signal, which also serves as electron spin initialization
Optically detected magnetic resonance (ODMR): spin-dependent photoluminescence signal, which also provides electron spin state readout
1970
1948
1990

## Slide 14
Optically addressable defect qubits
Material Platforms for Defect Qubits and Single Photon Emitters,
Gang Zhang, Yuan Cheng, Jyh-Pin Chou, and Adam Gali,
Applied Physics Reviews, 7, 031308 (2020)
Diamond NV center
Science 276, 2012 (1997)
SiC VSi (low contrast)
Nat. Mat. 14, 164 (2015)
SiC divacancy (high contrast)
Nature 479, 84 (2011)
Nat. Comm. 4, 1819 (2014)
Nat. Sci. Rev. 9, nwab122 (2022)
verified quantum bits
Room-temperature defect qubits
T-center
GaN centers (low and high contrasts)
Nat. Mat., 23, 512 (2024)
hBN (high contrast)
Nat. Mat., 23, 1379 (2024)
Nature, 643, 943 (2025)

## Slide 15
Optically addressable nitrogen-vacancy center in diamond
optically detected magnetic resonance (ODMR)
room temperature operation
  electron spin – nuclear spin registers
Science 314, 281 (2006)
T = 300K

## Slide 16
Optically addressable nitrogen-vacancy center in diamond
Room temperature quantum accelerator computation device (> 3 companies)

## Slide 17
Nitrogen-vacancy center in diamond: concept for AI algorithms
@ELTE: quantum simulator for realizing efficient AI algorithms

## Slide 18
Nitrogen-vacancy center in diamond: concept for AI algorithms
@Wigner RCP: proof of control single electron spin coupled to nuclear spins

## Slide 19
Summary & Challenges
Horizon Europe
Quantum computers can be realized in various platforms
Fault-tolerant quantum computers may be in reach but not yet realized
Quantum simulation is doable and can be useful
Diamond nitrogen-vacancy spins based quantum simulators for efficient AI algorithms
Device can be realized in Hungary

## Slide 20
Welcome to Budapest
MSCA (EU) postdoc award will be available
Defects in Solids for Semiconductor Technologies (DSQT 2026), June 8-12, 2026, Budapest, Hungary