## Slide 1
László Balázs
Gergely Surányi
Gergő Hamar
Dezső Varga
Wigner RCP
MUOGRAPHERS
2026
Budapest
Experiences with tomographic inversion of subsurface muographic measurements (bias and artifacts)
https://wigner.hu/s/high-energy-geophysics/
High-Energy Geophysics Research Group
Innovative gaseous detector development GROUP
Key words:
Regularization, Bias, Covariance, Artifacts

## Slide 2: Muon tomography: experiences (Muographic projects)
High-resolution measurements at
27 locations
Hundreds of measurement campaigns
High resolution measurements
In extreme environments

## Slide 3: Muon tomography: Muographic projects (Budapest, Hármashatár hill)
Hármashatár-hegy
Keleti oldal, 3D,
Bayesian L2-L2 reconstruction
Low-dynamic peripheral zone
reduced dynamic range

## Slide 4: Muon tomography: Muographic projects: Jánossy Underground Lab.
Vertical and horizontal ojects on 3D tomographic results
Reference measuring site with known geometry
(Bayesian L2-L2 reconstruction)
Standard deviation

## Slide 5: Muon tomography: What is causing the problem?
,
Limited azimuth range
(sampling problem)
Interchangeable subsets in the solution set (on the same set of trajectory)
Jacobian (permutation) symmetry (equivalences)
High-dimensional null space
Limited number of measuring position
with limited measirement time
Singular pseudo inverse
Regularization is necessary, with all that it entails
(with vertically oriented base vectors)
Nullity>Rank situation

## Slide 6: Muon tomography: Tomogrpahic inverse problem
Linearized direct problem
of discrete tomography
Pixel-voxel transformation
Density length error distribution
prior distribution
ML-term (loss)
Prior-term
The result vector is the weighted sum of the two types of information (flexibility)
Fisher-matrix
From the null space, prior selects one element ~ NS(prior)
(informative or noninformative,
generally smooth)
Unique solution with prior dependent bias

## Slide 7: Muon tomography: Error term: bias and variance
Bias
Parameter Covariance-matrix
Formally, variance and bias are linked through the covariance matrix
„Trade-off”
The source of bias is always a real anomaly
Posterior distribution
Result of regularization: Smoothing around the prior: dynamic range compression +
Fisher-matrix baked correlations
+
+
-
-
Localized inversion
Non localized inversion
„point” spread function (on Simulated 2D inversion)
Density range. [g/ccm}
Correlation spikes
Jánossy Lab.
Anomaly leak along the trajectories
Anomaly at the detector position: Compensation artifact

## Slide 8: Muon tomography: Algorithms and priors
SVD: Spectral Value Decomposition
Tikhonov-type regularization
Bayes-type estimation (Geologic prior)
Filtered Back Projection
Expectation Maximalization (MLEM)
Early stop Iterations
Minimum norm
Smoothness (spatial correlations)
Prior density distribution (large scale geology)
Z dependent
Fisher information dependent
Metric and pdf
Gauss or Mixed Gaussian L2 norm
Laplacean L1 norm
Key inversion algorithms
Prior
Because of fan-shaped imaging
Sparsity handling
+ bias reduction post process

## Slide 9: Muon tomography: Voxel grid and adaptive prior
The prior distribution relates to voxel based densities, so it depends on the voxel size.
Dependence requires an appropriate averaging model.
(scalable prior)
Averaging : small scale bias
Ro
Information loss and voxel split
An overly refined model increases the correlation among voxel elements. Changing the correlation structure (associated with the mapping) can reduce the rank of the Fisher matrix
Voxel grid – Hármashatár hill
Fisher-information
Muon trajectory

## Slide 10: Muon tomography: Simulation and tests
Chessboard-test
For focus range definition
(Bias mapping)
Fault-test for detectability
(Hármashatár hill)
The detection limit changes with the regularization parameters

## Slide 11: Muon tomography: Horizontal and vertical object distortion
unvisible
visible
Trajectory lengths [m]
In pixels
Inversion results
2D simulation in Janossy geometry (2D is the worst case in term of artifact)

## Slide 12: Muon tomography: Horizontal and vertical object distortion
unvisible
Visible
Trajectory lengths [m]
Inversion results
2D simulation in Janossy geometry
Not localizable

## Slide 13: Muon tomography: One-sided measurements
One-sided mapping – apparently tilted object + shadow zone
unvisible
unvisible
visible
visible
Shadow zone

## Slide 14: Muon tomography
An album of characteristic bias and artefacts
Thank you for your attention!

## Slide 18: Muon tomography: Focus range - Information distribution
Result
Sum of trajectory lengths [m]
No of overlaping detector cone
Relative Fisher-information
Standard dev. [g/ccm}
Density range. [g/ccm}

## Slide 19: Muon tomography: Extra
Justification of fault indication
Táró alaprajza