## Slide 1: Muon Tomography at 1 km - Hardware
Jean-Luc Gauvreau
Occidental College, Los Angeles, USA
Muographers 2026 – Budapest
June 3, 2026

## Slide 2
Air shower muography
To do muography you need θ, ɸ and depth of detection.
Depth is easy and cheap to measure if θ, ɸ could be measured in some other way.
Muons often arrive together in a pancake structure spread over length scales of ~100 m (air shower)
At depths > 25 m all detected muons are associated with a shower on the surface.
Notes: Gas Detector gives muon directional information but is expensive.
Using Low cost (non-directional) BH detectors coupled with a surface array we can detect air showers.
Angle is measured by the array while depth is measured by the BH detectors.
Protons of very high energies produce air showers with length scales ~ 100m
At depths > 25m all detected muons are associated with a surface air shower.

## Slide 3
Example of a muon air shower creating hits in
three surface detectors and one borehole detector.
muon path
D4
D2
D1
D3
BH1
BH2
Time
D1
D2
D3
Signal
t1
t2
t3
BH2
t4
electron path
Concept
Notes: Air showers: surface detectors detect electrons mostly
BH detectors at depths > 25m detect muons mostly.
In the example above, an incoming air shower hits 3 surface detectors and 1 BH detector
The resulting peaks would look as shown.

## Slide 4: Assembled Detector
16 scintillating bars from Fermi Lab
With total area of 1.5m2
32 Wavelength Shifting Optical Fibers
Onsemi 6mm x 6mm SiPM
Alex Clark and Haoran Sun assembling a detector at UI.
Onsemi 6mm x 6mm SiPM
Notes: The surface detectors were assembled at UI.
The bars were produced by extrusion at Fermi Lab. The bars have two holes lengthwise to insert 2 x 1mm fibers
The detector contains: 16 scintillating bars, 32 Wavelength shifting fibers, 2 SiPM boards, temp/hum sensors
We detect the light at both ends of the fibers
A Muon creates an ionizing track in a bar.
The light is captured by a fiber. The SiPMs transform the light pulses into an electric signal. The peaking time of the pulse is recorded using a 1GHz DRS digitizer or a GPS based time stamp.

## Slide 5: Assembly at UI
Ben Hooberman, Ipsita Chaudhary, Tim Healy and Alex Clark
12 detectors were assembled at UI.
Notes: Thanks to UI
Shown: Ben Hooberman, his student and two Oxy researchers.

## Slide 6: Assembly at UI
Fiber installation. Two per bar.
Fibers polished and ready for SiPM assembly
Bars and grooves installed.

## Slide 7: Final Assembly and Deployment ay Oxy
Notes: An electric box was added. It contains a GPS module and discrimination electronics.

## Slide 8: Array Deployment in Oxy Upper parking lot
10 detectors were deployed at Oxy.
Notes: Each detector was self-surveyed by its GPS over 24 hours.
Cross-checks were made using a Lidar and laser level.
The position accuracy is 15cm rms
Timing tests were made by sending a pulse per second between adjacent detectors.
The timing accuracy is ~ 2.5ns, mainly due to the inherent +/-4ns jitter of the GPS
The trailer contains a winch for the gas detector.
The borehole is located at the right end of the trailer.

## Slide 9: BH Scintillators
9cm x 50cm scintillator
SiPM board, no fiber.
Electric signal sent using a BNC cable.
Time stamp on the surface.

## Slide 10: Borehole Deployment
Sealed BH detectors
3 cylindrical scintillator BH deployed
1 directional gas detector
1 Veto scintillator
The borehole is 30m deep at Oxy

## Slide 11: Wavelength Shifting Fibers
Kuraray Y-11
  Absorption peak: 430nm (Blue)
  Emission peak: 476nm (Green)
  Attenuation length = 4m
  Diameter of fiber: 1mm

## Slide 12: Timing and Data Collection (Phase 1)
Timing: DRS acquisition
  time accuracy: 1ns
  4 channels per module
  Long BNC cables required
  Trigger from borehole
Data discrimination: by software
Data parsing: by software during post-analysis
Data transmission: BNC
Notes: For a large 1600 detector array, the cost of cables and labor may be prohibitive

## Slide 13: Timing and Data Collection (Phase 2)
Timing: GPS acquisition
  jitter: ± 4ns  accuracy: 2.3ns rms
  2 channels per module
  Self-survey spatial accuracy: 15cm
Data discrimination: by hardware
Data parsing: ESP32 μ-Processor
Data transmission: WiFi
Notes: No data cables, cheaper for a large array.

## Slide 14: Time and Angle Uncertainties
rms times | σt (ns)
Scintillator/Fiber | 1.7
Fiber Length | 2.6
SiPM + electronics | 2
GPS | 2.5
Total | 4.5
Estimated errors on angles using a simplified model for the current array :
Zenith: 3.4° rms
Azimuth: 3.7° rms
To be compared with Monte Carlo simulation and actual data in Dan Snowden-Ifft’s talk
Notes: We tabulated the sources of time uncertainties above.
If needed, with some efforts, we could reduce the total time uncertainty to ~ 3ns.

## Slide 15: Data Flow

## Slide 16
Muon rate: ~ 200Hz per surface detector
Array events are only sent to the server when coincident with a borehole event.
In post analysis, we identify events that have 4 hits or more.
The direction of the muon shower is obtained from the position and timing of the hits.
Actual shower detection rate in coincidence with a borehole: ~ 10-3 Hz
The data rate transmitted by WiFi is low.
Data Flow

## Slide 17: Map of directional muons
In red: Borehole detector
In blue: Surface detectors
Format: t1/t2(det#)
Arrow: Muon direction in x-y plane
Dotted lines: 10ns increments

## Slide 18: Improvements for a Completely Wireless Larger Array
1600 surface detectors over a circle of 1km radius
300 borehole detectors distributed over a depth of 1km.
Long range communication using Wifi HaLow
  Range > 1km
  Sub GHz frequency
  32.5 Mbps data rate
FPGA based acquisition
  ns resolution
  GPS as primary clock
Solar + Battery Powered
  5 watts per detector

## Slide 19: Thanks
Oxy Team:
Dan Snowden-Ifft, Alex Clark, Tim Healy, John Halloran, Jack Davis
Kobold Metals team:
Bill Page and Tom Hunt
UI Team:
Ben Hooberman, Haoran Sun, Ipsita Chaudhary, Prathik Boyella, Matthia Perdekamp

## Slide 20
Array events are only sent to the server when coincident with a borehole event.
In post analysis, we identify events that have 4 hits or more.
The direction of the muon shower is obtained from the position and timing of the hits.
Detector muon rate: ~ 200Hz per detector
Actual shower detection rate in coincidence with a borehole: ~ 10-3 Hz
CPU
GPS
Array
Detector 1
GPS
GPS
Base Station
CPU
CPU
Array
Detector 2
Borehole
Detector 1
Data Flow

## Slide 21
Array events are only sent to the server when coincident with a borehole event.
In post analysis, we identify events that have 4 hits or more.
The direction of the muon shower is obtained from the position and timing of the hits.
Detector muon rate: ~ 200Hz per detector
Actual shower detection rate in coincidence with a borehole: ~ 10-3 Hz
CPU
GPS
Array
Detector 1
GPS
GPS
Base Station
CPU
CPU
Array
Detector 2
Borehole
Detector 1
Data Flow

## Slide 22
Array events are only sent to the server when coincident with a borehole event.
In post analysis, we identify events that have 4 hits or more.
The direction of the muon shower is obtained from the position and timing of the hits.
Detector muon rate: ~ 200Hz per detector
Actual shower detection rate in coincidence with a borehole: ~ 10-3 Hz
Data Flow
CPU
GPS
Array
Detector 1
GPS
GPS
Base Station
CPU
CPU
Array
Detector 2
Borehole
Detector 1

## Slide 23
Array events are only sent to the server when coincident with a borehole event.
In post analysis, we identify events that have 4 hits or more.
The direction of the muon shower is obtained from the position and timing of the hits.
Detector muon rate: ~ 200Hz per detector
Actual shower detection rate in coincidence with a borehole: ~ 10-3 Hz
Data Flow
CPU
GPS
Array
Detector 1
GPS
GPS
Base Station
CPU
CPU
Array
Detector 2
Borehole
Detector 1

## Slide 24
Array events are only sent to the server when coincident with a borehole event.
In post analysis, we identify events that have 4 hits or more.
The direction of the muon shower is obtained from the position and timing of the hits.
Detector muon rate: ~ 200Hz per detector
Actual shower detection rate in coincidence with a borehole: ~ 10-3 Hz
Data Flow
CPU
GPS
Array
Detector 1
GPS
GPS
Base Station
CPU
CPU
Array
Detector 2
Borehole
Detector 1

## Slide 25
Array events are only sent to the server when coincident with a borehole event.
In post analysis, we identify events that have 4 hits or more.
The direction of the muon shower is obtained from the position and timing of the hits.
Detector muon rate: ~ 200Hz per detector
Actual shower detection rate in coincidence with a borehole: ~ 10-3 Hz
Data Flow
CPU
GPS
Array
Detector 1
GPS
GPS
Base Station
CPU
CPU
Array
Detector 2
Borehole
Detector 1

## Slide 26
Array events are only sent to the server when coincident with a borehole event.
In post analysis, we identify events that have 4 hits or more.
The direction of the muon shower is obtained from the position and timing of the hits.
Detector muon rate: ~ 200Hz per detector
Actual shower detection rate in coincidence with a borehole: ~ 10-3 Hz
Data Flow
CPU
GPS
Array
Detector 1
GPS
GPS
Base Station
CPU
CPU
Array
Detector 2
Borehole
Detector 1

## Slide 27
Array events are only sent to the server when coincident with a borehole event.
In post analysis, we identify events that have 4 hits or more.
The direction of the muon shower is obtained from the position and timing of the hits.
Detector muon rate: ~ 200Hz per detector
Actual shower detection rate in coincidence with a borehole: ~ 10-3 Hz
Data Flow
CPU
GPS
Array
Detector 1
GPS
GPS
Base Station
CPU
CPU
Array
Detector 2
Borehole
Detector 1

## Slide 28
Array events are only sent to the server when coincident with a borehole event.
In post analysis, we identify events that have 4 hits or more.
The direction of the muon shower is obtained from the position and timing of the hits.
Detector muon rate: ~ 200Hz per detector
Actual shower detection rate in coincidence with a borehole: ~ 10-3 Hz
Data Flow
CPU
GPS
Array
Detector 1
GPS
GPS
Base Station
CPU
CPU
Array
Detector 2
Borehole
Detector 1

## Slide 29
Array events are only sent to the server when coincident with a borehole event.
In post analysis, we identify events that have 4 hits or more.
The direction of the muon shower is obtained from the position and timing of the hits.
Detector muon rate: ~ 200Hz per detector
Actual shower detection rate in coincidence with a borehole: ~ 10-3 Hz
CPU
GPS
Array
Detector 1
GPS
GPS
Base Station
CPU
CPU
Array
Detector 2
Borehole
Detector 1
Data Flow

## Slide 30
Array events are only sent to the server when coincident with a borehole event.
In post analysis, we identify events that have 4 hits or more.
The direction of the muon shower is obtained from the position and timing of the hits.
Detector muon rate: ~ 200Hz per detector
Actual shower detection rate in coincidence with a borehole: ~ 10-3 Hz
Data Flow
CPU
GPS
Array
Detector 1
GPS
GPS
Base Station
CPU
CPU
Array
Detector 2
Borehole
Detector 1

## Slide 31
Array events are only sent to the server when coincident with a borehole event.
In post analysis, we identify events that have 4 hits or more.
The direction of the muon shower is obtained from the position and timing of the hits.
Detector muon rate: ~ 200Hz per detector
Actual shower detection rate in coincidence with a borehole: ~ 10-3 Hz
Data Flow
CPU
GPS
Array
Detector 1
GPS
GPS
Base Station
CPU
CPU
Array
Detector 2
Borehole
Detector 1

## Slide 32
Array events are only sent to the server when coincident with a borehole event.
In post analysis, we identify events that have 4 hits or more.
The direction of the muon shower is obtained from the position and timing of the hits.
Detector muon rate: ~ 200Hz per detector
Actual shower detection rate in coincidence with a borehole: ~ 10-3 Hz
Data Flow
CPU
GPS
Array
Detector 1
GPS
GPS
Base Station
CPU
CPU
Array
Detector 2
Borehole
Detector 1

## Slide 33
Array events are only sent to the server when coincident with a borehole event.
In post analysis, we identify events that have 4 hits or more.
The direction of the muon shower is obtained from the position and timing of the hits.
Detector muon rate: ~ 200Hz per detector
Actual shower detection rate in coincidence with a borehole: ~ 10-3 Hz
Data Flow
CPU
GPS
Array
Detector 1
GPS
GPS
Base Station
CPU
CPU
Array
Detector 2
Borehole
Detector 1