## Slide 1: Cosmic-ray-muon Scattering for Nuclear Material Measurement
Haruo Miyadera
Senior Manager Governor
Corporate Laboratory Toshiba Europe GmbH
Toshiba Corporation
Naoto Kume, Yuki Nakai, Kyohei Noguchi, Takuro Fujimaki, Tsukasa Sugita Fumihito Shinozaki
Toshiba Corporation
HN-2026-1710

## Slide 2: Cosmic-ray Muon Scattering Imaging
01

## Slide 3: Cosmic-ray Muon
Pions (p+, p-) generated when cosmic rays collide with the Earth’s atmosphere
Pions decay into muons (m+, m-)
Muons have relatively long life time of 2.2 ms
    Relativistic effect helps them survive to the Earth’s surface
  Cosmic-ray muon
    Muons are the major components of cosmic ray at the surface
    Muon flux: 10,000 /m2·min
    Accounts for 20％ of annual dose
Image from cosmic.lbl.gov
Primary cosmic ray
Pions
Muons
Chart: Energy[GeV]
Chart: Zenith angle [degree]

## Slide 4: Muon’s Interaction with Material
Energy loss and multiple Coulomb scattering are the major interactions of muon
Energy loss
  Muon losses energy through interaction with atomic/molecular electrons
    -dE/dx depends on electron density
Multiple Coulomb scattering
  Muons are distorted by interaction with nuclear charge
  Scattering angle:
    Larger the Z, larger the scattering angle
    Depends on material
Material
Low energy muon
High energy muon
Energy loss
Muon stop
Energy loss
Transmitted
Multiple Coulomb scatterings
Material
Direction changed
x=material length
X0=radiation length of material
βcp＝muon energy
Chart: [mrad]
| Air | Water | C | Concrete | Al | Fe | Pb | U
散乱角θ | 0.021575 | 0.71006 | 0.98093 | 1.2799 | 1.4651 | 3.3876 | 6.1089 | 8.2094
Scattering Angle

## Slide 5: Muon Imaging - Transmission Method
Transmission Method is muon roentgenography.
  Mine overburden, E.P. George (1955).
  Egyptian pyramid, L.W. Alvarez (1970).
  Temple gate, S. Minato (1988).
  Density map of volcano, K. Nagamine (1995).
  Blast furnace, K. Nagamine (2005).
Attenuation of muon flux
  Resolution degraded by continuous scattering
  along the muon path.
  Sometimes, incident muon flux not easy
  to estimate.
K. Nagamine, et al., Nucl. Instr. and Meth. A 356 (1995) 585.

## Slide 6: Muon Scattering Imaging Develop at LANL
Muon scattering angle provides material information
(1) Location of scatterer identified by point-of-closest-approach
(2) Scattering angle provides material info
  Scattering angle approximately scales with atominc number
Muon tracker
Muon tracker
Container (low Z)
High-Z material
(1) PoCA identifies the location
(2) Scattering angle provides
material info
q0 scattering angle βc velocity p momentum
x material thickness X0: radiation length
Container
Scanner
C. Morris et al., Science & Global Security 16, 37 (2008).
10,000 muon/m2·min at the surface
Muon
Fe
Pb
min sec

## Slide 7: Material Identification of Scattering Method
Energy loss and scattering combined for material identification
C. Morris et al., AIP Advances 3, 082128 (2013).
Energy Loss obtained by muon attenuation
Radiation Length obtained by muon scattering angle
Radiation Length

## Slide 8: Muon Tracker for Scattering Imaging
High energy physics + nuclear ＋ consumer technologies
Muon
Drift tube detector
（High energy physics）
Detection
Area
Amplifier
（Nuclear technology）
Analysis
Muon tracking
Image output
Material identification
FPGA
（Consumer technology）

## Slide 9: Muon Trackers Developed at TOSHIBA
Gold
Drug A
Mock
nuclear
material
Explosive B
Toxic material C
Muon trackers
3.5mx3.5m
7m x 7m muon tracker for reactor imaging
  Collaborative effort with LANL and DSIC
  6,720 drift tubes used
  Can operate under radiation environment of
  50 mSv/h
Muon trackers
7mx7m
2015
3.5m x 3.5m muon tracker for R&D
  1,680 drift tubes used
  Non-destructive evaluation of infrastructures
  Material accounting
2020
Fukushima Daiichi muon imaging project was carried out as a part of “Project of Decommissioning and Contaminated Water Management” supported by Ministry of Economy, Trade and Industry, Japan.
https://www.global.toshiba/jp/news/corporate/2015/03/pr2701.html

## Slide 10: Muon Container Scanner
Detect smuggling across borders
Muon container scanners were installed at:
・Bahama ・Singapore
・UAE ・US – Mexico border
Muon container scanner assembly
Mock gold
■Gold
■Lead
■Steel
Steel
Lead
X [mm]
Material
identification
by AI
X
Y
Z
Y [mm]
Detected object
Z [mm]
Detection area
Detector modules
Oil
Oil + UO2
Truck

## Slide 11: Reactor Imaging at TOSHIBA Nuclear Critical Assembly
World’s first muon reactor imaging with real UO2 core
Technical demo with “real” reactor core at TOSHIBA’s research reactor.
Mini Muon Tracker of 1.2m x 1.2m size shipped from LANL and was installed to NCA.
Core
0.4m
Muon tracker
Muon tracker
Core
Steel/concrete
bricks
Fuel
Tank
Muon
C.Morris et al., APL 104, 024110 (2014).
T.Sugita et al., JNST 51, 7-8 (2014).
TOSHIBA Nuclear Critical Assembly
(Kawasaki, Japan)

## Slide 12: Nuclear Security
Muon technology capable of identifying fuel assemblies inside a cask
Most of the plutonium on earth is stored in steel dry-storage
casks of a few meter in diameter
Fuel assemblies inside a dry cask can be imaged
by muon scattering imaging
J.M Durham et al., Physical Review Applied 9,
044013 (2018)
LANL news 2018
Fuel assembly
in a cask
Muon trackers
D. Poulson et al., NIM A 842, 17 (2017).

## Slide 13: Material Accounting of Fukushima Daiichi’s Nuclear Debris using Cosmic-ray Muon Scattering
02
Haruo Miyadera
Naoto Kume, Yuki Nakai, Kyohei Noguchi, Takuro Fujimaki, Tsukasa Sugita, Fumihito Shinozaki
Toshiba Corporation
Shin Takasaki, Takahiro Tanaka, Ryunosuke Mizuguchi
Tousou Mirai Technology Company Limited (Decom.Tech)
This research was implemented under the Decommissioning, Contaminated Water and Treated Water Management project supported by Ministry of Economy, Trade and Industry, Japan.

## Slide 14: Fuel Debris in Fukushima Daiichi Decommissioning
Fuel debris will be retrieved and stored safely during Fukushima Daiichi decommissioning
No established technology exists to non-destructively estimate nuclear fuel content in debris
Retrieved materials may include structural components with adhered molten fuel
Measurement is hindered by materials such as control rods (neutron absorbers) and moisture
Sand
Structure material with adhered debris
Peddle
Pedestal
inner wall
A portion of a fuel assembly
Peddle
debris
Peddle
debris
Control Rod Drive
housing support parts
Photo source: TEPCO “48th and 50th Secretariat Meeting of the Decommissioning and Contaminated Water Countermeasures Team”

## Slide 15: Amount of Nuclear Fuel Needs to be Estimated
Can muon scattering measure amount of nuclear fuel?
It is desirable to measure amounts of nuclear fuel in the removed debris from Fukushima Daiichi
Muon Tracker
Muon Tracker
Muon
Debris container
Muon
Uniform
Non-
uniform
Non-
uniform
Mid-and-Long-Term Roadmap towards the
Decommissioning of TEPCO's Fukushima Daiichi
Nuclear Power Station Units 1-4
METI
Radiation
Detector
Radiation
Detector

## Slide 16: Measurement of Nuclear Material inside Debris is Challenging
Non-destructive measurement of debris inside a container
  Gammas and neutrons are measurable
    However it is not easy to estimate amounts of nuclear materials inside debris
Materials distributed non-uniformly
Different burn up
Contaminated structural materials
・Radiations depends on the burn up
・Radiations coming from everywhere
・Different elements and densities
・Self shielding effect
・Neutron deceleration
and capture
Nuclear fuel
Structural materials
Container
Debris inside container
Challenges measuring amount of nuclear materials

## Slide 17: Muon Scattering Method to Measure Uranium Contents in Debris
Prototype detector developed for mock-debris demonstration
Prototype muon scanner
1.2x1.2m2 detection area
Uranium
Muon Tracking under Radiation Environment
Left: track Hough transformation (blue dashed line), χ2 minimization of line fit (red solid line) and true muon track (black dashed line).
Right: Hough voting histogram and position obtained by χ2 minimization (red cross) and true muon track (black circle). Each drift tube is assumed to suffer 40-kHz noise which corresponds to the g environment of 200 mSv/h .
H. Miyadera et al., Applied Optics 63 (2024) A52.

## Slide 18: Analysis to Estimate Uranium Contents
UO2 contents can be obtained by solving simultaneous equations
<Debris analysis>
<Analysis>
Four equations on total weight, volume and average scattering angle:
where f(x) and R(x) give correlations between average muon scattering angles and attenuation, and material weights.
H: high Z
M: medium Z
L: low z
Classify into three elements: high Z, medium Z and low Z
UO2, SUS304 and concrete chosen as representative high-Z, medium-Z and low-Z materials
Uranium contents cannot be determined just by the muon scattering angle.
Analysis using total weight and volume of debris, muon scattering and attenuation developed.
Amount of nuclear fuel in the measurement [kg]
SUS304 + Uranium
Uranium
Concrete + Uranium
Estimated amount [kg]
Material | Density [g/cm3] | Classification
Pb | 11.35 | High Z
UO2 | 10.96 | 
SUS304 | 7.93 | Meddeum Z
Gd2O3 | 7.41 | 
ZrO2 | 5.68 | 
Al | 2.70 | Low Z
B4C | 2.52 | 
Concrete | 2.30 | 
H2O | 1.00 | 
Air | 0.0012 | -
3 hours measurement
Error bar: 3s

## Slide 19: Conclusion and Future Prospect
Material identification based on muon scattering has been applied to cargo scanner, detection of pipe valve without stopping the plant operation and inspection of reinforced concrete
Since muon scattering is sensitive to high-Z materials, muon scattering imaging is very useful for nuclear industry
  Core monitor for SMR
  Nuclear security such as dry cask imaging
Feasibility study performed to apply muon scattering to estimate amounts of nuclear materials in debris
A pair of prototype muon trackers are currently under development. Technical demonstrations with simulated debris carried out.