## Slide 1: ET: the Einstein Telescope
Harald Lück
Wigner111 September 12, 2013, Budapest
Image by Nikhef
Designing the third Generation of Gravitational Wave Detectors

## Slide 2: The advanced GW Network
Adv. Virgo, Cascina, 3 km
aLIGO Hanford, 4 km
aLIGO Livingston, 4 km
aLIGO INDIA 4km
KAGRA 3km
GEO600, Hannover, 600 m
LIGO and Virgo are being upgraded now to advanced versions and KAGRA is being built
Notes: KAGRA the former LCGT detector, a 3km cryogenic interferometer is being constructed in Japan in the Kamioka mine.
One of the LIGO Hanford detectors will most likely be transferred to India.

## Slide 3: Sensitivites: 1st and 2nd Gen.
KAGRA

## Slide 4: Noise sources limiting advanced detectors (example aLIGO, broadband)
10
1
10
2
10
3
10
−24
10
−23
10
−22
Frequency [Hz]
Strain [1/√Hz]
AdvLIGO Noise Curve: P
in
= 125.0 W
LIGO-T070247

## Slide 5
Einstein Telescope Conceptual Design Study
supported by the European Commission under the FP7-design studies framework
May 2008 – May 2011
Pan European effort
Science Team = ca. 250 members
http://www.et-gw.eu/etdsdocument
Notes: Going beyond what is possible with the current infrastructure
Underground and larger in size

## Slide 6: The Size
The Einstein Telescope will have 10 km arms
 gain a factor 2.5 w.r.t. advanced LIGO
LASER
Advanced LIGO
4 km
Einstein Telescope
10 km

## Slide 7: Low frequencies
7
NEWTONIAN NOISE
SEISMIC NOISE
Credit M.Lorenzini
Virgo and advanced Virgo seismic filtering is already close to the required performance
  Longer suspensions to improve low frequency isolation
Newtonian Noise
SEISMIC WAVE
Gravity gradient noise bypasses the seismic filtering

## Slide 8: Gravity Gradient noise in AdV
The GGN noise can limit the AdV sensitivity during days with high seismic activity:
M. Punturo (VIR-0073B-12)
M.Beker (GWADW 2012

## Slide 9
GGN analytical and FEA studies
Giancarlo Cella (2011)
  Analytical studies
  Giancarlo Cella
  Jan Harms
FEA modeling
  Mark Beker
  All wave types
  GGN drops slightly
  Little geometric
  suppression
Conclusions
  Challenge at low frequency
  Low seismic velocity is beneficial
  Studies for homogeneous media
Slide: Jo v.d. Brand

## Slide 10
ET seismic requirements
  5 x10-10 m/f2
Underground sites
  Several 100 m
Location w.r.t. oceans
Population density
Geology
Mark Beker, David Rabeling, Nikhef
Fulvio Ricci et al., Roma1
Low Frequencies
Seismic Noise

## Slide 11: Go Underground
Credit: Nikhef
ET Baseline: Build 200m under ground

## Slide 12: Mid- and high Frequencies
10
1
10
2
10
3
10
−24
10
−23
10
−22
Frequency [Hz]
Strain [1/√Hz]
AdvLIGO Noise Curve: P
in
= 125.0 W
LIGO-T070247
Shot Noise (high power) and Thermal Noise (low temperature)

## Slide 13: Mid- and High frequencies
Need High Power for Shot Noise
3MW
Need Cryogenics for Thermal Noise
10K
jgindo.wordpress.com
http://s658.photobucket.com
Notes: High Power disagrees with Cryo requirements

## Slide 14: ET Xylophone STrategy
10K, 18kW, 1550nm
300K, 3MW, 1064nm
Split detector into two interferometers optimised for
Low Frequencies
and
High Frequencies

## Slide 15: ET-D Xylophone sensitivity
Combining the two interferometers
ET-D-LF
ET-D-HF

## Slide 16: ET-D high frequency detector
Quantum noise: 3MW, tuned Signal-Recyling, 10dB Squeezing, 200kg fused silica mirrors.
Suspension Thermal and Seismic: Superattenuator (standard Virgo)
Gravity gradient: No Subtraction needed
Thermal noise: 290K, 12cm beam radius, fused Silica, LG33 (reduction factor of 1.6 compared to TEM00).
Coating Brownian reduction factors (compared to 2G):
3.3 (arm length), 2 (beam size) and 1.6 (LG33) = 10.5
Shot Noise reduction factors (compared to 2G):
1.6 (arm length), 1.9 (power), 3.2 (squeezing (10dB)) = 9.7

## Slide 17: ET-D low frequency detector
Quantum noise: 18kW, detuned Signal-Recyling, 10 dB frequency dependent Squeezing, 211kg mirrors.
Seismic: extended Superattenuator, 17m tall
Gravity gradient: no subtraction assumed in noise curve
Mirror thermal : 10K, Silicon, 12cm beam radius, TEM00.
Suspension Thermal: penultimate mass@2K, 3mm diameter silicon fibres, 2m long; limiting noise contribution from 1Hz-10Hz
As mirror TN is no longer limiting, one could relax the assumptions on the material parameters and the beam size…
Slide: Christian Gräf, ET Symp., 2013; modified

## Slide 18: SQUEEZING
Add filter cavities to have benefit at high AND low frequencies
Squeezing
10 dB Squeezing (baseline ET) is a challenge in terms of optical losses:
Starting with 20dB the overall losses from the crystal to the photo diode, including filter cavities, must be less then 9%.
(10 dB)

## Slide 19: Mechanical losses of substrates
 High Q-factor at both room temperature and cryogenic temperatures
Credits: Ronny Nawrodt
ET Baseline

## Slide 20: Large Silicon Substrates
Source: http://www.iisb.fraunhofer.de/content/dam/iisb/de/images/geschaeftsfelder/halbleiterfertigungsgeraete_und_methoden/gadest_2011/
450 mm
300 mm
Source: http://www.quora.com/Semiconductors/How-do-silicon-boules-not-break-off-during-semiconductor-fabrication
Large Silicon Substrates are available but only in CZ grown Crystals.
Whether the purity reachable is sufficient is currently being tested

## Slide 21: Heavy Silicon Boules
Source: www.pvatepla.com
Silicon Boules can be grown to a weight of 450kg

## Slide 22: Silicon absorption
Requires pure (float zone) material
Inconsistent measurements across groups
Indications for enhanced absorption close to surfaces
Under investigation
4ppm/cm
OPTICS LETTERS / Vol. 38, No. 12 / June 15, 2013

## Slide 23: Coating Research
Standard SiO2/Ta2O5 dominate Thermal Noise
Amorphous coatings (Tantala dominated)
  Research for improving at room temperature
    Understanding loss mechanisms
    Empirical studies, doping with other materials
    Annealing
    Researching alternative materials (e.g. Zirkonia, Hafnia, Niobia)
Crystalline Coatings
  AlGaAs
  GaP/AlGaP
Waveguide structures

## Slide 24
AlGaAs Coatings
Promising results at cryogenic temperature
Thermo-optic (=Thermoelastic + refractive) noise at high frequencies
Need many, thin layers
Same overall thickness as standard
Reach low optical absoprtion Finesse ca. 100.000
Graphics credit: G. Cole
Need to be grown on GaAs and then transferred to Si substrate
Potential for large substrates demonstrated
Risk of detaching

## Slide 25: GaP/AlGaP Coatings
GaP/AlGaP mirrors can be grown directly on Si
Need a buffer layer GaP for lattice matching
Promising first results: Low losses @ Cryo T
Tantala
GaP -layer
Upper limit of loss for GaP on Si, Credit: A. Lin 45x lower than undoped SiO2/Ta2O5

## Slide 26: Waveguide coatings
Avoid lossy thick coating
Have not reached required reflectivity yet
Mechanical losses look promising

## Slide 27: Sensitivites: 1st, 2nd and 3rd Gen.
KAGRA

## Slide 28: Sensitivites: 1st, 2nd and 3rd Gen.
KAGRA
LIGO 3G
Notes: Assumption is that basically the same infrastructure will be used

## Slide 29
GW Timelines
 | ´06 | ´07 | ´08 | ´09 | ´10 | ´11 | ´12 | ´13 | ´14 | ´15 | ´16 | ´17 | ´18 | ´19 | ´20 | ´21 | ´22 | ´23 | ´24 | ´25 |  | 
Virgo |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
GEO |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
LIGO |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
KAGRA |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
E.T. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Hanford
Livingston
You are here
2nd Generation
DS
PCP
Construction
Comm.
data
Site Prep.
3rd Generation
India
E-LIGO
Advanced LIGO
GEO 600
Virgo+
Advanced Virgo
LIGO 3G?
1st Generation
´26
´27

## Slide 30: Einstein telescope New technologies
ET is based mostly on mature proven technology
  Longer arms („1.5“x10km) & underground
  Higher power than advanced detectors (3 MW)
  Cryogenic optics for low thermal noise
  Split into two (Xylophone) to make Cryo and MW compatible
  Larger, heavier optics; HOM (LG33) beams;
  Laser Wavelength (Silicon:1550nm; fused Silica: 1064nm)
  Frequency dependent squeezing
  No new coatings in baseline concept, but will be used as state of the art allows

## Slide 31
Einstein Telescope

## Slide 32: 1st, 2nd 2+, and 3rd generation
LIGO 3G

## Slide 33
ICRR
EGO
UniRoma
MPG
FSU
FOM
Uni Glasgow
UniSannio
UWS
http://www.et-gw.eu/descriptionelites

## Slide 34
WP1, "Cryogenics and suspensions",
  Measure of the performance of designed cryogenic suspension system in a practical interferometer from the point of seismic and vibration isolation
  Design and test of auxiliary attenuation system for thermal link
WP2, "Mirror thermal noise and cryogenics
  Investigation of the mechanical loss in both silicon and sapphire bulk materials;
  Performance of suitable optical coatings on sapphire substrates for the development of the mirrors for LCGT and to share the complimentary expertise contained within the LCGT and ET groups (e.g. Japanese expertise in studying low temperature properties of sapphire, European expertise in studying low temperature coatings)
  Assessment of the properties and suitability of silicate bonding for bonding sapphire, and comparison with the properties of bonded silicon, to develop techniques for constructing sapphire suspensions for use in LCGT and as a possible alternate suspension material for use in ET
  Characterisation of the thermal and mechanical properties of suspension elements (fibres, bond areas, etc.)
WP3, "Large-scale cryogenic infrastructure for LCGT and ET“
  Specifying noise sources arising from cooling system quantatively and qualitatively
  Optimum design of raditation shield
  Prevention of possbile contamination of clean surface of mirrors

## Slide 35: ET R&D Project
EGO
UniRoma
MPG
FSU
FOM
UGla
Napoli
UWS
http://www.et-gw.eu/etrddescription
MSU
INR RAS
LMA
ARTEMIS
UW
WUT
PAoS
Bham
Cardiff
Zielona
Bialistok
Baksan
INFN Pisa
KFKI
Germany
Netherlands
Russia
Poland
United Kingdom
Italy
France
Hungary
Notes: MSU-SAI: Sternberg Astronomical Institute (lead)
MSU-PD: Physics Department INR RAS: Institute of Nuclear Research Russian Academy of Science
University of Warsaw (lead),
University of Zielona Gora,
University of Bialystok, Warsaw University of Technology,
Polish Academy of Science (Inst. of Mathematics), PAoS(Nicolaus Copernicus Astronomical Centre)
KFKI Research Institute for Particle and Nuclear Science
Geodetic and Geophysical Research Institute

## Slide 36
Working Projects
WP1, "ET’s scientific potential"
  Mock ET data and science challenges of increasing complexity
  Explore how well astrophysical models of GW sources could be tested with ET
  Investigate possible strong field tests of GR with ET
  Probe ET’s potential for understanding the geometry and dynamics of the Universe
WP2, "Long term seismic and GGN studies of selected sites“
  Studies at candidate sites
  Sensor and network development
  Modeling of seismic and GGN noise
WP3, "Optical properties of silicon at cryogenic temperatures"
  Stress induced birefringence of silicon-based optic
  Homogeneity of optical properties within larger samples
  Investigation of Whispering Gallery Mode Oscillators made of silicon to probe absorption and scattering
WP4, "ET Control systems“
  Mitigation scheme for radiation pressure effects for the ET-HF interferometer.
  Control scheme for the injection of frequency dependent squeezed light.
  Low-frequency control scheme for the ET-LF interferometer.
  Mitigation scheme for correlated noise in co-located interferometers.
  Contamination of potential null stream signals by technical noises.
ET R&D Project