## Slide 1: GRAVITATIONAL WAVE EXPERIMENTS
István Rácz
RMKI
Wigner Virgo group

## Slide 2: Talk Outline
Introduction to the Gravitational Wave (GW) search
Gravitational wave detectors
  Today
  Near future
The aim of the game: gravitational wave astronomy
Perspectives

## Slide 3: General Relativity and GW
GW are predicted by the Einstein General Relativity
  GR is a metric theory of gravity
to the matter source Tmn
(energy-momentum tensor)
Einstein field equation links Gmn
Using appropriate gauge: Einstein field equations can be seen to form a set of coupled nonlinear wave equations.
Far from the sources, linear approximation and radiation gauge can be used, yielding wave equation for the perturbation of the background geometry

## Slide 4: Gravitational Waves
GWs are deformations of the spacetime geometry propagating with the speed of light
Two polarizations: h+ & h
The effect of GWs on a mass distribution is the modulation of the reciprocal distance of the masses
h
h+

## Slide 5: But, do GWs really exist?
Neutron star binary system: PSR1913+16
  Pulsar bound to a “dark companion”
  7 kpc from Earth, relativistic: vmax/c ~10-3
Nobel Prize 1993: Hulse and Taylor
  GR predicts such a system to loose energy via GW emission: orbital period decrease
  Radiative prediction of general relativity verified at 0.2% level

## Slide 6: GW detectors: the resonant bars
The epoch of the GW detectors began with the resonant bars
Joseph Weber (~1960)
Resonant bar suspended in the middle
Then a network of cryogenic bars has been developed in the past
Piezoelectric transducers

## Slide 7: GW interferometric detectors
A worldwide network of detectors has been developed:
KAGRA, Kamioke,
3 km, 2.5 gen.
GEO, Hannover, 600 m
LIGO Livingston, 4 km
Virgo, Cascina, 3 km
LIGO Hanford, 4 km: 2 ITF àt the same site!

## Slide 8: Working principle
The quadrupolar nature of the GW makes the Michelson interferometer a “natural” GW detector
E1
E2
Ein
102L0 104 m in terrestrial detectors
Typical wave length ~100km
We need a “trick” to construct such a detector on the Earth
Fabry-Perot
cavity
Effective length:

## Slide 9: How small is 10-18 m?
Size of the Universe
Virgo cluster
Galactic center
Target GW wavelengths
Neutron star radius
Wavelength of YAG laser
Size of an atom
Proton radius
Virgo sensitivity
1 Light-year
log10 r

## Slide 10: Detector sensitivity
The faint space-time deformation measurement must compete with a series of noise sources that are spoiling the detector sensitivity
Seismic filtering:
in Virgo pendulum chains to reduce seismic motion by a factor 1014 above 10 Hz
Virgo nominal
sensitivity
~10 m

## Slide 11: Detector sensitivity
The faint space-time deformation measurement must compete with a series of noise sources that are spoiling the detector sensitivity
Optimization of the payload design to minimize the mechanical losses

## Slide 12: Detector sensitivity
The faint space-time deformation measurement must compete with a series of noise sources that are spoiling the detector sensitivity
Maximization of the injected laser power, to minimize the shot noise

## Slide 13: A real detector scheme
Laser 20 W
Output Mode Cleaner, ~1W
3 km long Fabry-Perot cavities:
to lengthen the optical path to
100 km, ~50 kW
Input Mode Cleaner
Power recycling mirror:
to increase the light power
to 1 kW
Virgo optical scheme

## Slide 14
Master laser, 1W
Slave laser, 22W
Main Beam Path
F.I.
E.O.
F.I.
F.I.
Laser

## Slide 15
Fused silica mirrors
35 cm diam, 10 cm thick, 21 kg
Scattering losses: a few ppm
Substrate losses: 1 ppm
Coating losses: <5 ppm
Surface deformation: /100
Super mirrors

## Slide 16
Requirements
10-9 mbar for total pressure
10-14 mbar for hydrocarbons
Vacuum enclosure
7000 m3

## Slide 17: Sensitivity: real life
Virgo+ noise budget example

## Slide 18: Virgo sensitivity evolution

## Slide 19
VIRGO
LAPP – Annecy
NIKHEF – Amsterdam
GPG – Birmingham
INFN – Firenze-Urbino
INFN – Frascati
INFN – Genoa
INFN – Perugia
INFN – Pisa
INFN – Roma 1
INFN – Roma 2
Univ of Warsav
Wigner - Budapest
The VIRGO collaboration
IPN – Lyon
INFN – Napoli
OCA – Nice
LAL – Orsay
ESPCI – Paris
APC – Paris
INFN – Padova-Trento

## Slide 20
Thousands of galaxis in the distance ~50 million light years
LOW EXPECTED EVENT RATE:
0.01-0.1 ev/yr (NS-NS)
1ST GENERATION INTERFEROMETERS CAN
DETECT A NS-NS COALESCENCE
AS FAR AS VIRGO CLUSTER (15 MPc)

## Slide 21: Benefits by the LIGO-Virgo network
Triangulation allowing to pinpoint the source
A network allows to measure signal parameters, including source distance for BNS signals
Avoide false alarm coincidence
Joint operation yields a longer observation time, and a better sky coverage
Notes: 21

## Slide 22: GW sources: isolated NS
Isolated NS are a possible source of GW if they have a non-null quadrupolar moment (ellipticity)
Crab pulsar in the Crab nebula (2kpc)
LIGO-S5 upper limit: 6% of the SD limit in energy
Vela pulsar in its nebula (0.3kpc)
Spin-down limit to be determined in the Virgo VSR2-VSR3 runs
Credits: C.Palomba

## Slide 23: 1st generation GW detector nominal sensitivities

## Slide 24: GW interferometer past evolution
Detection distance (a.u.)
Evolution of the GW detectors (Virgo example):
2003
Infrastructure realization and detector assembling
2008
Same
infrastructure
Proof of the working principle
Commissioning
& first runs
year
Upper Limit physics

## Slide 25: GW interferometer present evolution
enhanceddetectors
Evolution of the GW detectors (Virgo example):
2003
Infrastructure realization and detector assembling
2008
Same
infrastructure
Justification of he working principle
Upper Limit physics
2011
Same
infrastructure
Test of “advanced” techs
UL physics
2017
Same
infrastructure
Advanced
detectors
First detection
Initial astrophysics
Commissioning
& first runs
Detection distance (a.u.)
year

## Slide 26: Advanced detectors
  Increase of the BNS detection distance from 20MPc to 200 MPc
  A BNS detection rate ~ 10/year with a limited SNR:
  The beating of the spin-down limit for many known pulsars
108 ly
Enhanced LIGO/Virgo+
Virgo/LIGO
Credit: R.Powell, B.Berger
Adv. Virgo/Adv. LIGO
Credits: C.Palomba

## Slide 27: Virgo upgrade plans
08
09
10
11
12
13
14
15
16
Virgo+ installation
Advanced Virgo
Virgo+
Virgo Science Run 2
Virgo+ commissioning
Installation of monolithic suspensions (?)
Virgo Science Run 3
Advanced Virgo installation
Advanced Virgo commissioning
Advanced Virgo Science Run 1
08
10
12
14
16
18
100
101
102
103
yr
Mpc
BNS inpiral range – expected progress

## Slide 28: Advanced Detectors will see GWs
The technology of interferometric detectors has been demonstrated
A further step in sensitivity appears necessary to open the way to physics and astronomy. Some sources appear certain, unless astrophysical assumptions are wrong
To make science, a multimessenger approach will be mandatory

## Slide 29: 3rd generation?
Evolution of the GW detectors (Virgo example):
2003
Infrastructure realization and detector assembling
2008
Same
infrastructure
Proof of the working principle
Upper Limit physics
2011
enhanceddetectors
Same
infrastructure
Test of “advanced” techs
UL physics
2017
Same
infrastructure
Advanced
detectors
First detection
Initial astrophysics
2022
Same
Infrastructure
(20 years old for Virgo, even more for LIGO & GEO600)
Commissioning
& first runs
Precision Astrophysics
Cosmology
?
Detection distance (a.u.)
year
Limit of the current infrastructures

## Slide 30: GW Astronomy ?
Current e.m. telescopes are mapping the Universe in all the wavelengths detectable from the Earth and from the space but mainly the outer region is known.
  Truly dynamical processes are hidden inside stars, only indirect methods
94% of the universe is dark. Composed by either dark energy or dark matter. The dark part interact via gravitation.
Gravitational wave telescopes could complement the e.m. observation opening the GW astrophysics era.
Thanks to the small interaction between graviton and the matter, GW are the best messenger to investigate the first instants of the Universe.
visible
Infrared
408MHz
WMAP
X-ray
g-ray
GRB
GW ?

## Slide 31: Physics Beyond GW Detections
Astrophysics:
  Measure in great detail the physical parameters of the stellar bodies composing the binary systems
    NS-NS, NS-BH, BH-BH
    Constrain the Equation of State of NS through the measurement
      of the merging phase of BNS
      of the NS stellar modes
      of the gravitational continuous wave emitted by a pulsar NS
  Contribute to solve the GRB enigma
Relativity
  Compare the numerical relativity model describing the coalescence of intermediate mass black holes
  Test General Relativity against other gravitation theories
Cosmology
  Measure few cosmological parameters using the GW signal from BNS emitting also an e.m. signal (like GRB)
  Probe the first instant of the universe and its evolution through the measurement of the GW stochastic background
Astro-particle:
  Contribute to the measure the neutrino mass?
  Constrain the graviton mass measurement

## Slide 32: Measuring Properties of Neutron-Stars with GWs
In GR properties of NSs are determined by the equation of state (EoS) via TOV equation
  Nuclear model, laboratory experiment
  Astrophysical observations
  NS merger: EoS should yield imprint on the emitted GW signal

## Slide 33
Orientation averaged spectra
Notice the EoS dependence of fpeak

## Slide 34
Peak frequency vs radius of MNS=1.35xMsun (left)
  fpeak is higher for smaller radius !!!
fpeak vs , M𝑡𝑜𝑡=2 MNS (right)
Values of R and MNS can be inferred from the pre-merger PN part of the wave form

## Slide 35
0.1m 10m 1 Hz 100 10k
4x107 4x105 4x103 M 40 0.4
frequency f / binary black hole mass whose freq at merger=f
1st generation detectors
3rd generation
Advanced detectors
10-22
10-23
10-24
10-25
h (1/√Hz)‏
Credit: B.Sathyaprakash
2009
2015-6
2020
2028?
eLISA

## Slide 36: The infrastructure
Pictorial view
~100 m
Thanks for your attention